## Slide 1: Chapter: Regulations, Codes and Standars
Notes: <number>
Chapter 10
Title: Regulations, Codes and Standards
Level: Basic
Requisites: none
Overall aim: The chapter gives an overview of the major standards.
Content
1. International standards
2. Technical committees
3. Specific standards
4. Directives
Learning outcomes
The student will be able to
identify the major standards associated with fuel cell technologies
identify the organizations responsible for developing the standards
Methodology: Lectures, group work, discussion
Schedule: 1 one - hour - unit

## Slide 2: CONTENTS
Introduction.
Hydrogen Technologies.
2.1 Standard of Hydrogen Technologies.
Cryogenic Vessels.
Combustible Gases (lighter than air).
Voltage regulations.
Electrical Noise.
ISO TC 197.
IEC TC 105 Fuel cells.
SAE Standards for automotive fuel cell.
Hydrogen fuelling and fuelling stations.
Notes: <number>

## Slide 3
International Organizations for Standardisation : There are many international standards organizations, but the three international organizations having the highest international recognition are:
the International Standards Organization (ISO),
the International Electrotechnical Commission (IEC),
the International Telecommunication Union (ITU).
1. Introduction
The European Standards Organisations are CEN, CENELEC and ETSI.
  CEN is the officially recognized standardization representative for sectors other than electrotechnical (CENELEC) and telecommunications (ETSI).
  EASC - Euro-Asian Council for Standardization, Metrology and Certification.
  IRMM - Institute for Reference Materials and Measurements.
B
Notes: <number>
The three International Standards Organizations have established tens of thousands of standards covering almost every conceivable topic. Many of these are then adopted worldwide replacing various incompatible 'homegrown' standards. Many of these standards are naturally evolved from those designed in-house within an industry, or by a particular country, whilst others have been built from scratch by groups of experts who sit on various technical committees (TCs).
ISO is composed of the National Standards Bodies (NSBs), one per member economy.
The IEC is composed of “National Committees”, one per member economy.
In some cases, the National Committee to the IEC of an economy may be the ISO member from that country or economy.
The World Standards Cooperation (WSC) is a cooperative effort between ISO, the IEC, and the ITU.
In addition to these organizations, there exist thousands of standards organizations that set standards within some more specialized context, such as IETF, W3C, IEEE or API.
Often, these international standards organizations are not based on the principle of one member per country. Rather, membership in such international organizations is more granular having either organizational/corporate or individual technical expert members from around the globe.
In general, each country or economy has a single recognized Standards Body (NSB).
NSBs may be either public or private sector organizations, or combinations of the two. For example, the three NSBs of Canada, Mexico and the United States are respectively the Standards Council of Canada (SCC), the General Bureau of Standards and the American National Standards Institute (ANSI).
Standardization activities USA
  SAE: fuel cell standards committee
  ANSI/CSA FC 1 2005 (fuel cell power plants and other applications)
  NFPA 853 (installation of stationary FC power plants)
  ASME PTC 50 (performance test code for FC power system performance)
European Directives and Standards:
EN 59465 (<70 kW fuel cell CHP plants); somehow in competition with ANSI/CSA FC-4
http://www.newapproach.org/ProductFamilies/Keywords.asp
http://www.eihp.org/

## Slide 4
2. Hydrogen Technologies
ISO has three Committees for Standardisation related to Hydrogen:
ISO/TC 197 about “Hydrogen technologies”.
ISO/TC 58 about “Gas cylinders”.
ISO/TC 22 about “Road vehicles”.
TC 22/SC21 “Electric, hybrid and fuel cell vehicles”.
TC 22/SC25 “Road vehicles using LPG, CMG, H2”.
IEC has two Committees for Standardisation related to Hydrogen:
IEC/TC 105 about fuel cells.
IEC/TC 69 about electric systems.
There are important directives and standards regarding stationary hydrogen technologies and infrastructure:
ATEX Directives, (95 nand 137).
PED (Pressurised Equipment Directive),
EMC (electromagnetic compatibility) Directive,
The Machinery Safety Directive,
SEVESO II (large amounts of haz. mat.), 96/082/EEC.
B
Notes: <number>
There are more organizations which information, security recommendations,… about hydrogen, fuel cells and related technologies to.
The American National Standards Institute (ANSI) has developed standards related to hydrogen and compressed gases:
NACE
Standard TM0284-96, item N°21215, Standard test method, Evaluation of pipeline and pressure vessel steels for resistance to hydrogen-induced cracking
Standard RP0177-95: Mitigation of Alternating Current and Lightning Effects on Metallic Structures and Corrosion Control Systems
Standard RP01-98: Control of corrosion under thermal installation and fire proofing material
Standard RP05 02: Pipeline external corrosion direct assessment methodology
EIGA: European Industrial Gases Association: Provide Authorities and Standardisation bodies with expert advice on production, transport, storage and applications of industrial and medical gases. Promote consistency of safety, health, environmental and technical standards throughout the industrial gas industry
TN 26/81: Hydrogen cylinders and transport vessels
DOC 15/96: Gaseous hydrogen stations
DOC 75/01: Determination of safety distances
http://hcsp.ansi.org/
http://fuelcellstandars.com (Hydrogen Codes and Standars Portal, U.S.A.)
http://www.hydrogenandfuelcellsafety.info/
http://www.eiga.be/
Standarization work for fuel cells in Road vehicles is mainly done within the SAE framework.

## Slide 5
2. Hydrogen Technologies
2.1 Standard of Hydrogen Technologies
ISO 13984:1999 Liquid hydrogen - Land vehicle fuelling system interface.
ISO 13985:2006 Liquid hydrogen - Land vehicle fuel tanks.
ISO 14687:1999/Cor 1:2001 Hydrogen fuel - Product specification.
ISO/PAS 15594:2004 Airport hydrogen fuelling facility operations.
ISO/TR 15916:2004 Basic considerations for the safety of hydrogen systems.
ISO 16110-1:2007 Hydrogen generators using fuel processing technologies - Part 1: Safety.
ISO/TS 16111:2006 Transportable gas storage devices - Hydrogen absorbed in reversible metal hydride.
ISO 17268:2006 Compressed hydrogen surface vehicle refuelling connection devices.
B
Notes: <number>
ISO and IEC standards are required for:
•H2 production equipment: ISO/TC 197
• Service stations: ISO/TC 197
Filling connectors : ISO/TC 197 and ISO/TC 22
• Fuel cells: IEC/TC 105
Onboard H2/FC equipment:ISO/TC 197, ISO/TC 22 and IEC/TC105

## Slide 6
Working Drafts:
ISO/WD 22734 Hydrogen generators using water electrolysis process.
ISO WD 13986 Tank containers for multimodal transportation of liquid hydrogen.
Committee Drafts:
ISO/CD PAS 15594 Airport hydrogen fuelling facility.
ISO/ CD 22734 Electrolyzer.
ISO/CD 24490 Cryogenics pump.
Draft Publicly Available Specification:
ISO/PRF TR 15916 Basic considerations for safety of hydrogen systems.
Proposed New Work Items:
ISO/AWI 16110 Hydrogen generators using fuel processing technologies.
ISO/AWI 16111 Transportable gas storage devices – Hydrogen absorbed in reversible metal hydride.
ISO/TC 197 NWIP N 253 Dispensing Unit.
ISO/NP 20012 Gaseous hydrogen and hydrogen blends — Fuelling stations (Draft Technical Specification).
2. Hydrogen Technologies
B
Notes: <number>
Other International Standards related to:
ISO 13623: Petroleum and natural gas industries-Pipeline transportation systems
ISO 9809: Cylinder design
ISO 11120: Jumbo tubes design
ISO/DIS 15869 Gaseous hydrogen and hydrogen blends – Land vehicle fuel tanks –
ISO/DIS 17268 Gaseous hydrogen – Land vehicle filling connectors (based on SAE J2600)
ISO/ DIS 21009- 1 Liquid hydrogen storage
ISO/DPAS 15594 Airport hydrogen fuelling facility
ISO/WD 15866 Gaseous hydrogen and hydrogen blends -- Service stations
ISO /WD 22734 Hydrogen generators using water electrolysis process
ISO/CD 15869 Gaseous hydrogen and hydrogen blends – Land Vehicle fuel tanks

## Slide 7
.
3. Cryogenic Vessels
European Standards
Directive 97/23/EC and Harmonised Standard EN 13458 provide framework requirements for the pressure protection of cryogenic storage tank systems.
EN 13458-1, Cryogenic vessels - Static vacuum insulated vessels -Part 1: Fundamental requirements.
EN 13458-2, Cryogenic vessels - Static vacuum insulated vessels -Part 2: Design, fabrication, inspection and testing.
EN 13458-3, Cryogenic vessels - Static vacuum insulated vessels -Part 3: Operational requirements.
EN 14197-3 , Cryogenic vessels – Static non vacuum insulated vessels–Part 3: Operational.
EN 13648-3: Cryogenic vessels – Safety devices for protection against excessive pressure – part 3: Determination of required discharge capacity and sizing for relief devices.
B
Notes: <number>
CRYOGENIC VESSELS
Requirements
For each of the static cryogenic vessel the following data shall be available: manufacturer, serial number(s), date of manufacture, regulation to which the static cryogenic vessels were designed and manufactured, certificates concerning manufacturing, material and tests, working pressure [pS], test pressure [pT], diameter of the inner vessel, minimum wall thickness of the inner vessel, water capacity , product(s) for which the static cryogenic vessel is designed and manufactured.
European Cryogenic Vessels Standards (CEN/TC 268) can be checked:
http://www.cen.eu/newapproach/cen/stdlist.asp?dir_area=97/23/EC&prod_fam=CEN/TC%20268
http://ec.europa.eu/enterprise/newapproach/standardization/harmstds/reflist.html
Inspections
In order to verify the equivalent level of safety the inspection body shall ensure that:
the above list contains sufficient information necessary to reassess the static cryogenic vessels,
the wall thickness of the static cryogenic vessels is equal to or greater than the minimum thickness as calculated in accordance with EN 13458-1 and -2 (this may require the adjustment working pressure),
the static cryogenic vessel was pressure tested with a pressure not less than the required value pneumatic test in accordance with EN 13458-1 and -2.
In addition a periodic inspection in accordance with EN 13458-3 shall be carried out.
IGC Document TN 23/79, Recommendations for the periodic inspection and testing of cryogenic vessels.
ISO/TC 220 Cryogenic vessels

## Slide 8
4. Combustible Gases
(lighter than air)
Gases lighter than air: N2, CO,C2H4, B2H6, HCN, C2H2, Ne, HF, NH3, CH4, He, H2
Pressure Equipment Directive (97/23/EC),
Properties, Handling, Storage, Safety,
Simple pressure vessels (87/404/EC)
Transportable Pressure Equipment Directive (1999/36/EC TPED)
Transportable gas cylinders- 93/42/EEC
B
Notes: <number>
Directive (97/23/EC),
Properties, Handling, Storage, Safety,
http://ec.europa.eu/enterprise/pressure_equipment/ped/directive/index_en.html
Simple pressure vessels (87/404/EC)
http://ec.europa.eu/enterprise/pressure_equipment/spvd_sector/index_en.html
Transportable gas cylinders- 89/106/EEC
European Standars related to these technologies:
ISO/TC 58 Gas cylinders
ISO/TC 58/SC 3 Gas cylinder design
ISO TC 11boilers and pressure vessels
ISO TC 118: Compressors, pneumatic tools and pneumatic
ISO TC 153: Valves
EN1594: Gas supply systems- Pipelines for maximum operating pressures over 16 bar
EN 14161: same as ISO 13623
EN 10208-2: Steel pipes for pipelines for combustible fluids
EN 12954: Cathodic protection of buried or immersed metallic structures
EN10285: Steel tubes and fittings for on and offshore pipelines- External three layer extruded polyethylene based coatings
EN12732: Gas supply systems.Welding steel pipework- Functional requirements
EN60079-10: Electrical apparatus for explosive gas atmospheres- Part 10: Classification of hazardous Areas
EN60079-14: Electrical apparatus for explosive gas atmospheres- Part 14: Electrical installations in hazardous areas
EN61508: Functional safety of electrical/electronic/programmable electronic safety related systems
EN ISO 11114-1 Compatibility of cylinder and valve materials with gas contents Part 1: Metallic Materials
EN ISO 11114-2 Compatibility of cylinder and valve materials with gas contents Part2: Non Metallic Materials
EN ISO 11114-4:2005 Transportable gas cylinders - Compatibility of cylinder and valve materials with gas contents - Part 4: Test methods for selecting metallic materials resistant to hydrogen embrittlement
EN 1968 Periodic Inspection and testing of seamless steel gas cylinders
ISO 6506-1 Metallic materials -- Brinell hardness test -- Part 1: Test method
EN 13769 Gas Cylinders Stamp Marking
http://ec.europa.eu/enterprise/newapproach/standardization/harmstds/reflist.html

## Slide 9
5. Voltage regulations
Low Voltage Equipment Directive 2006/95/EC (previously 73/23/EEC).
  Scope of the Low Voltage Directive: The Low Voltage Directive applies to 'electrical equipment' designed for use with a voltage rating of between 50 and 1000 V for alternating current and between 75 and 1500 V for direct current.
See Also: Directive 94/9/EC (ATEX 100)
B
Notes: <number>
Low Voltage Directive:
Equipment and phenomena outside the scope of the Directive:
Electrical equipment for use in an explosive atmosphere;
Electrical equipment for radiology and medical purposes;
Electrical parts for goods and passenger lifts;
Electricity meters;
Plugs and socket outlets for domestic use;
Electric fence controllers;
Radio-electrical interference;
Specialized electrical equipment, for use on ships, aircraft or railways, which complies with the safety provisions drawn up by international bodies in which the Member States participate.
Principal elements of the safety objectives for electrical equipment designed for use within certain voltage limits are:
general conditions;
protection against hazards arising from the electrical equipment;
protection against hazards which may be caused by external influences on the electrical equipment.
High voltage regulations
Measures taken to prevent such explosions include:
Intrinsic safety, which is apparatus designed to not accumulate enough stored energy to touch off an explosion
Increased safety, which applies to devices using measures such as oil-filled enclosures to prevent contact between sparking apparatus and an explosive atmosphere
Explosion-proof enclosures, which are designed so that an explosion within the enclosure cannot escape and touch off the surrounding atmosphere (this designation does not imply that the apparatus will survive an internal or external explosion).
Electrical equipment including transfer pump motor and lighting of compartments shall be suitable for hydrogen service, e.g. explosion proof or inerted. This does not apply to the automotive electrics
ISO/TC 203 Technical energy systems
http://europa.eu.int/comm/dgs/energy_transport

## Slide 10
6. Electrical Noise
Noise Emitted by Machines and Equipment (IEC)
Directive 89/336/EEC (it has been amended by Directive 91/263/EEC, Directive 92/31/EEC and Directive 93/68/EEC. )
http://ec.europa.eu/enterprise/electr_equipment/emc/directiv/dir336.htm
The new EMC Directive 2004/108/EC has been published in the Official Journal of the European Union, L 390/24, 31 December 2004, and will repeal Directive 89/336/EEC as from 20 July 2007
B
Notes: <number>
European Standards related to electrical Noise can be looked up:
http://ec.europa.eu/enterprise/newapproach/standardization/harmstds/reflist/emc.html

## Slide 11
7. ISO TC 197
Scope of the ISO/TC 197
ISO/TC 197 was created to promote the increased use of hydrogen as an energy carrier and fuel.
Standardization in the field of systems and devices for the production, storage, transport, measurement and use of hydrogen.
The standardization efforts of the technical committee ISO/TC 197 will facilitate the emergence of a renewable, sustainable energy system based upon hydrogen as an energy carrier and fuel.
As standardization is undertaken simultaneously with technology development, ISO/TC 197 work will facilitate the early demonstration
and implementation of the hydrogen technologies that will be required to move hydrogen into widespread energy applications.
B
Notes: <number>
ISO/TC 197 was originally created to accompany the development of the technologies that are related to the use of hydrogen as an energy carrier and fuel.
the objectives of the technical committee in the next years are the following:
Elaboration of standards on the product specification of the hydrogen fuel.
2. Elaboration of generic standards that will provide the guidelines for the development of a hydrogen distribution and storage infrastructure. Storage technologies for mobile and stationary applications (multimodal containers, nanotubes and metal hydrides), refuelling stations, hydrogen pipeline, etc. should be standardized.
3. Elaboration of standards or collaboration to the development of the standards on the end-use applications (fuel cells, internal combustion engines, hydrogen burners).
4. Collaboration to the development of standards on hydrogen devices dedicated for use onboard road vehicles (road vehicle fuel tanks, fuelling connectors).
5. Elaboration of standards on the relevant properties of hydrogen and the safety considerations related to the presence of hydrogen
6. Elaboration of standards on the hydrogen production technologies from renewable primary sources such as hydropower, solar energy, wind power and the small-scale hydrogen production technologies from fossil fuels such as small-scale steam reformers.
7. Elaboration of standards on detection devices (electronic detectors) and safety related devices (pressure
relief valves, shut-off valves, pressure regulators, etc.) of generic use to be used in hydrogen systems.

## Slide 12
7. ISO TC 197
Working Drafts:
WG6 15869 (IS) Gaseous hydrogen and hydrogen blends — Land vehicle fuel tanks.
WG5 17268 (revision IS) Compressed hydrogen surface vehicle refuelling connection devices.
WG8 22734-1 (IS) Hydrogen generators using water electrolysis process — Part 1: Industrial and commercial applications.
WG8 22734-2 (IS) Hydrogen generators using water electrolysis process — Part 2: Residential applications.
WG9 16110-2 (IS) Hydrogen generators using fuel processing technologies — Part 2: Test methods for performance.
WG10 16111 (IS) Transportable gas storage devices — Hydrogen absorbed in reversible metal hydrides.
WG11 20012 (TS) Gaseous hydrogen — Fuelling stations.
WG12 14687-2 (IS) Hydrogen Fuel — Product Specification — Part 2: PEM fuel cell applications for road vehicles.
WG13 26142 (IS) Hydrogen detectors.
New issues:
Transportable gas storage devices – Hydrogen absorbed in reversible metal hydride.
Gaseous hydrogen – Hydrogen generators using fuel processing technologies.
B
Notes: <number>

## Slide 13
8. IEC TC 105 Fuel cells
IEC 62282, which is a technical specification, has been prepared by IEC technical committee 105: Fuel cell technologies, consists of the following parts under the general title Fuel cell technologies:
Part 1: Terminology.
Part 2: Fuel cell modules.
Part 3-1: Stationary fuel cell power plants – Safety.
Part 3-2: Stationary fuel cell power plants – Test methods for performance.
Part 3-3: Stationary fuel cell power plants – Installation.
Part 4: Fuel cell system for propulsion and auxiliary power units.
Part 5: Portable fuel cell appliances – Safety and performance requirements.
Part 6-1: Micro fuel cell power systems – Safety1.
Part 6-2: Micro fuel cell power systems – Performance1.
Part 6-3: Micro fuel cell power systems – Interchangeability1.
Part 7-1: Single Cell Test Method for Polymer Electrolyte Fuel Cell (PEFC).
B
Notes: <number>
Part 1: Terminology
Provides uniform terminology in the forms of diagrams, definitions and equations related to fuel cell technologies in all applications including but not limited to stationary power, transportation, portable power and micro power applications. Is intended as a resource for the Working Groups and users of the IEC 62282 series of fuel cell standards.
Part 2: Fuel cell modules
This part of IEC 62282 provides the minimum requirements for safety and performance of fuel cell modules. This standard applies to fuel cell modules with the following electrolyte
chemistry: alkaline; proton exchange membrane (including direct methanol fuel cells); phosphoric acid; molten carbonate; solid oxide fuel cell modules.
IEC 62282-am1: Amendment 1 - Fuel cell technologies - Part 2: Fuel cell modules
Part 3-1: Stationary fuel cell power plants – Safety1
This part of IEC 62282 is a product safety standard suitable for conformity assessment as stated in IEC Guide 104:1997, ISO/IEC Guide 51:1999 and ISO/IEC Guide 7:1994.
Part 3-2: Stationary fuel cell power plants – Test methods for the performance
This part of IEC 62282 covers operational and environmental aspects of the stationary fuel cell power systems performance. The test methods apply as follows:
– power output under specified operating and transient conditions;
– electrical and thermal efficiency under specified operating conditions;
– environmental characteristics; for example, gas emissions, noise, etc. under specified
operating and transient conditions.
Coverage for Electromagnetic Compatibility (EMC) is not provided in this part of IEC 62282.
Part 3-3: Stationary fuel cell power plants – Installation1
Part 4: Fuel cell system for propulsion and auxiliary power units

## Slide 14
8. IEC TC 105 Fuel cells
IEC 62282 consists of the following parts under the general title Fuel cell technologies:
Part 1: Terminology.
Part 2: Fuel cell modules.
Part 3-1: Stationary fuel cell power plants – Safety.
Part 3-2: Stationary fuel cell power plants – Test methods for performance.
Part 3-3: Stationary fuel cell power plants – Installation.
Part 4: Fuel cell system for propulsion and auxiliary power units.
Part 5: Portable fuel cell appliances – Safety and performance requirements.
Part 6-1: Micro fuel cell power systems – Safety1.
Part 6-2: Micro fuel cell power systems – Performance1.
Part 6-3: Micro fuel cell power systems – Interchangeability1.
Part 7-1: Single Cell Test Method for Polymer Electrolyte Fuel Cell (PEFC).
B
Notes: <number>
Part 5-1: Portable fuel cell appliances – Safety requirements
This part of IEC 62282 covers construction, marking and test requirements for a.c. and d.c.
type portable fuel cell systems. These fuel cell systems are movable and not fastened or
otherwise secured to a specific location. The purpose of the portable fuel cell system is to
produce useable power.
This standard applies to a.c. and d.c. type portable fuel cell systems, with a rated output
voltage not exceeding 600 V a.c., or 850 V d.c. for indoor and outdoor use in a non-hazardous
area.
Part 6-1: Micro fuel cell power systems – Safety1
Establishes requirements for all fuel cell power systems, units and cartridges to ensure a reasonable degree of safety for normal use, reasonably foreseeable misuse, and consumer transportation of such items. Covers fuel cell power systems, power units and fuel cartridges that are wearable or easily carried by hand, providing d.c. outputs not exceeding 60 V d.c. and power outputs not exceeding 240 VA.
Part 6-2: Micro fuel cell power systems – Performance1
This Final Draft International Standard has the following voting period: 2007-08-03 to 2007-10-05 for being published.
Part 6-3: Micro fuel cell power systems – Interchangeability1
This Final Draft International Standard has the following voting period: 2007-08-17 to 2007-10-19 for being published.
Part 7-1: Single Cell Test Method for Polymer Electrolyte Fuel Cell (PEFC)
More information and drafts of the documents:
http://webstore.iec.ch/webstore/webstore.nsf/searchview/?searchView=&SearchOrder=4&SearchWV=TRUE&SearchMax=1000&Submit=OK&Query=(%5BICS_Code_List%5D=27.070)

## Slide 15
Road Vehicle
Industry
Suppliers Industry &
SAE
Joint scope of work:
safety
performance
energy consumption
emissions
IEC/TC105
Fuel Cell
Industry
ISO/TC22
SC21
9. SAE Standards for automotive fuel cell
44 directives have to be applied in order to receive an approval for a road vehicle in Europe.
If a vehicle is successfully tested according to these 44 EC directives or equivalent ECE regulations it has to be approved.
B
Notes: <number>
Society of Automotive Engineers (SAE): SAE standards for automotive fuel cell (Standards information: http://www.sae.org/fuelcells/fuelcells.htm )
Working Groups: 1. Performance, 2. Emissions & Fuel Consumption, 3. Interface: Hydrogen Quality Task Force, 4. Recyclability, 5. Safety, 6.Terminology
SAE J2600: Compressed Hydrogen Surface Vehicle Refuelling Connection Devices. It applies to design, safety and operation verification of Compressed Hydrogen Surface Vehicle (CHSV) refuelling connection devices hereinafter referred to as nozzle and receptacle
SAE J2578 Recommended Practice for General Fuel Cell Vehicle Safety. This SAE Recommended Practice identifies and defines the preferred technical guidelines relating to the safe integration of fuel cell system, fuel storage, and electrical systems into the overall Fuel Cell Vehicle. Purpose The purpose of this document is to provide introductory mechanical and electrical system safety guidelines that should be considered when designing fuel cell vehicles for use on public roads. Field of Application This document covers fuel cell vehicles designed for use on public roads.
SAE J2574 Fuel Cell Vehicle Technology. This SAE Information Report contains definitions for hydrogen fuel cell powered vehicle terminology. It is intended that this document be a resource for those writing other hydrogen fuel cell vehicle documents, specifically, Standards or Recommended Practices.
Standards ISO
ISO TC 22: Road vehicles
SC 21: Electric road vehicles
  WG1: Vehicle operation conditions, vehicle safety and energy storage installation
  WG2: Terminology. Definitions and methods of measurement of vehicle performance and of energy consumption
European Integrated Hydrogen Project-Phase II (EIHP2) http://www.eihp.org

## Slide 16
10. Hydrogen fuelling and fuelling stations
Hydrogen stations are to be considered as subject to a particular risk of fire and explosion.
The degree of risk influences the type of electrical installation.
The installation and operation of electrical systems in hydrogen stations must be in accordance with the Regulations, Standards and Codes of Practice of each country.
In particular ATEX Directive must be taken into account for this application.
B
Notes: <number>
ISO 17268:2006 Compressed hydrogen surface vehicle refuelling connection devices
Existing European Standards (CENELEC) covering electrical apparatus for potentially explosive
atmospheres are:
• EN 50 014 General requirements
• EN 50 015 Oil immersion
• EN 50 016 Pressurised apparatus
• EN 50 017 Powder filling
• EN 50 018 Flame-proof enclosure
• EN 50 019 Increased safety
• EN 50 020 Intrinsic safety
Source: http://www.eiga.org/home2.asp

## Slide 17
11. ATEX: Explosive atmosphere regulations
Directive 99/92 EC ATEX 137A
Directive 94/9/EC ATEX 100
EN 60079-10, Electrical apparatus for explosive gas atmospheres. Part 10: Classification of hazardous areas.
EN 1127-1:1997 , Explosive atmospheres – explosion prevention and protection –Identifies thirteen different ignition sources, which are separated in two groups, one with the ones more relevant for the industrial gases.
EN 13463-1, Non-electrical equipment for potentially explosive atmospheres – Part 1: Basic methods and requirements.
EN 26184-2:1991 Explosion protection systems - Part 2 : Determination of explosion indices of combustible gases in air (ISO 6184-2:1985)No89/106/EEC.
The EN standard gives more detailed information concerning protective requirements for equipment in different zones: http://ec.europa.eu/enterprise/newapproach/standardization/harmstds/reflist/atex.html
B
Notes: <number>
ATEX 137A workplace directive 99/92/EC, Minimum requirements for improving the safety and health protection of workers potentially at risk from explosive atmospheres.
The directive specifies the minimum requirements for the protection of workers potentially at risk from explosive atmosphere.
ATEX 100 equipment directive 94/9/EC, Equipment and protective systems intended for use in potentially explosive atmospheres; This Directive is issued in order to harmonize the interpretation of EU Directive 1999/92. However, it is necessary to review the content of the EU Directive 94/9 due to its high importance for work in areas with a risk for explosive atmosphere. The directive 94/9 concerning (mechanical and electrical) equipment and protective systems intended for use in potentially explosive areas is valid when the equipment has an own source of ignition of any kind. Directive applies only to new equipment and systems that are placed on the market after 1 July 2003.
In very broad terms, there are three pre-conditions for the Directive to apply: the equipment a) must have its own source of ignition; b) be intended for use in a potentially explosive atmosphere (air mixtures); and c) be under normal atmospheric conditions.
The Directive also covers components essential for the safe use and safety devices directly contributing to the safe use of the equipment in scope. These latter devices may be outside the potentially explosive environment.
EU guide "Non-binding guide of good practice for implementing Directive 1999/92
http://www.europa.eu.int/comm/employment_social/health_safety/legislation_en.htm
EU guide "Non-binding guide of good practice for implementing Directive 94/9
http://ec.europa.eu/enterprise/atex/guide/atexguidelines_may2007.pdf
http://europa.eu.int/comm/enterprise/atex/guide.htm
PrEN 1839, Determination of explosion limits of gases, vapours and their mixtures
PrEN 13673-2, Determination of maximum explosion pressure and maximum explosion pressure rise of gases and vapours – Part 2: Determination of the maximum explosion pressure rise
PrEN 13980 Potentially explosive atmospheres – Application of quality systems
TR 50404, Electrostatics – Code of practice for the avoidance of hazards due to static electricity, CENELEC, 2003.

## Slide 18
12. International Cooperation
B
Notes: <number>
Cooperations
Established close collaboration with other organizations to address fuel infrastructure application system and national/ regional activities.
Joint Co-ordination Group JCG TC82/TC21/TC88/(TC105)
  Decentralised Renewable Energy Systems
liaisons with…
  ISO/TC197 (Hydrogen)
  ISO/TC22/SC 21 (Electric Road Vehicles)
  SAE International (FC Committee)
  IEC/TC31 (Electric Apparatus in Explosive Atmospheres, informal)