## Slide 1: Chapter : Hydrogen Economy Background
In this chapter you get a brief overview of 1. World Energy Supply and Demand, 2. World Energy Reserves, 3. Development of Renewable Energy in Europe, 4. Environmental Problems like Global CO2-Challenge, Green House Effect and Local Air Pollution.
And it gives an outlook on possible solutions: 5. Reduction of Demand before Supply and 6. Hydrogen Economy: Visions, System Components, Benefits and Challenges
Notes: Chapter 1
Title: Hydrogen Economy Background
Level: Basic, (mainly) intermediate, advanced
Requisites: a solid understanding of energy matters
Overall aim: In this chapter you get a brief overview of World Energy Supply and Demand, World Energy Reserves, Development of Renewable Energy in Europe, Environmental Problems like Global CO2-Challenge, Green House Effect and Local Air Pollution. And it gives an outlook on possible solutions: Reduction of Demand before Supply and Hydrogen Economy: Visions, System Components, Benefits and Challenges.
Content
    World Energy Supply and Demand by End-use Sectors, Regions and Fuels
    World Energy Reserves
    Development of Renewable Energy in Europe
    Environmental Problems:
        Global CO2-Challenge: Risks, Emissions, Green House Effect
        Local Air Pollution
    First Solution: Reduction of Demand before Supply
    Hydrogen Economy: Visions, System Components, Benefits and Challenges
        Socio-economic aspects
        Environmental aspects
Learning outcomes
The student will able to
roughly understand energy economy framework like world energy supply and demand, reserves and renewables
Generally understand environmental problems like Global CO2-Challenge, Green House Effect and Local Air Pollution
understand principle solutions to the energy challenges
To follow the vision of a hydrogen based economy and discuss its pros and cons
Methodology: Lectures, group work, discussion
Schedule: 4 one - hour – units (minimum, better more)

## Slide 2: Outline
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
World Energy Supply and Demand by End-use Sectors, Regions and Fuels
World Energy Reserves
Development of Renewable Energy in Europe
Environmental Problems:
    Global CO2-Challenge: Risks, Emissions, Green House Effect
    Local Air Pollution
First Solution: Reduction of Demand before Supply
Hydrogen Economy: Visions, System Components, Benefits and Challenges
    Socio-economic aspects
    Environmental aspects
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 3: # 1: World Energy Supply and Demand by End-use Sectors, Regions and Fuels
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6

## Slide 4: Global Primary Energy 1850 – 2000 and Key Technologies
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: Nakicenovic 2006
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: Nakicenovic 2006 Global Energy Perspectives to 2050 and Beyond, presented at International Conference within Autrian EU Presidency „Energy Path – Horizon 2050“, Vienna 6th March 2006

## Slide 5: World total primary energy supply by Region 1971-2030
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: IEA 2006
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: For explanations and background info: EIA (US)_International Energy Outlook 2006_Highlights.pdf (4 pages, file attached)

## Slide 6: World Delivered Energy Consumption by End-Use Sector, 2003-2030
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
Source: EIA (US) 2006
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: International Energy Outlook 2006 (Sources: 2003: Derived from Energy Information Administration (EIA), International Energy Annual 2003 (May-July 2005), web site www.eia.doe.gov/iea/. 2010-2030: EIA, System for the Analysis of Global Energy Markets (2006))
For explanations and background info: EIA (US)_International Energy Outlook 2006_Highlights.pdf (4 pages, file attached)

## Slide 7: World Marketed Primary Energy Use by Fuel, 1980-2030
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: EIA (US) 2006
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: International Energy Outlook 2006 (Sources: History: Energy Information Administration (EIA), International Energy Annual 2003 (May-July 2005), web site www.eia.doe.gov/iea/. Projections: EIA, System for the Analysis of Global Energy Markets (2006))
For explanations and background info: EIA (US)_International Energy Outlook 2006_Highlights.pdf (4 pages, file attached)

## Slide 8: World Energy Consumption for Electricity Generation by Fuel Type, 2003, 2015, and 2030
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: EIA (US) 2006
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: International Energy Outlook 2006 (Sources: 2003: Derived from Energy Information Administration (EIA), International Energy Annual 2003 (May-July 2005), web site www.eia.doe.gov/iea/. 2010-2030: EIA, System for the Analysis of Global Energy Markets (2006))
For explanations and background info: EIA (US)_International Energy Outlook 2006_Highlights.pdf (4 pages, file attached)

## Slide 9: # 2: World Energy Reserves
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6

## Slide 10: Categories of Energy Reserves
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I

## Slide 11: WORLD PRIMARY ENERGY USE AND RESERVES (2001)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: Updated from WEA 2000
A
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
* 1 toe = 42GJ. a. Based on constant production and static reserves. b. Includes both conventional and unconventional reserves and resources.
c. Data refer to the energy use of a business-as-usual scenario—that is, production is dynamic and a function of demand. Thus these ratios are subject to change under different scenarios. Dynamic resource base – production was calculated based on a 2 percent growth rate per year from 2000 to peak production (oil 6.1 Gtoe, gas 6.3 Gtoe, and coal 8.9 Gtoe), followed by a 2 percent decline per year until the resource base is exhausted.
d. Includes modern biomass, small hydropower, geothermal energy, wind energy, solar energy, and marine energy. Modern biomass accounts for 6.0 exajoules; 2.9 exajoules comes from all other renewables. “Modern biomass” refers to biomass produced in a sustainable way and used for electricity generation, heat production, and transportation (liquid fuels). It includes wood/forest residues from reforestation and/or sustainable management, rural (animal and agricultural) and urban residues (including solid waste and liquid effluents); it does not include traditional uses of fuelwood in inefficient and pollutant conversion systems. e. Converted from electricity produced to fuels consumed assuming a 33 percent thermal efficiency of power plants. f. Based on once-through uranium fuel cycles excluding thorium and low-concentration uranium from seawater. The uranium resource base is theoretically 60 times larger if fast breeder reactors are used.

## Slide 12: Evolution of Global Primary Energy Consumption
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: Nakicenovic 2006
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: Nebosja Nakicenovic 2006 Global Energy Perspectives to 2050 and Beyond, presented at International Conference within Austrian EU Presidency „Energy Path – Horizon 2050“, Vienna 6th March 2006.

## Slide 13: Solar Radiation and Fossil Reserves in Comparison to Yearly World Energy Demand
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: Greenpeace
World Resources:
Gas
Oil
Coal
Uranium
World Energy Demand/year
Solar Radiation on earth/ year
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: The cubes in the illustration represent fossil energy ressources, yearly solar radiation onto the earth surface and yearly world energy demand. The different sizes give an indication of the ressources available in relation to the yearly demand.
The solar radiation onto earth each year (big blue cube) exceeds the yearly world energy demand (small white cube in the right bottom corner) by three orders of magnitude.
Equally the yearly solar radiation onto earth is 2 to 3 orders of magnitude bigger than the total world fossil ressources of gas, oil, coal and uranium.
From this, we can follow, that solar supply is exceedingly sufficient to meet the world energy demand. Provided that we learn better, how to harvest the free solar energy have.
H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 14: # 3: Development of Renewable Energy in Europe
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6

## Slide 15: Development of Renewable Primary Energy Production in Europe (in %)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: STATE OF RENEWABLE ENERGIES IN EUROPE – 2006 EurObserv'ER
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
A 4,9 % GROWTH FOR RENEWABLE PRIMARY ENERGY
1. RENEWABLE ORIGIN PRIMARY ENERGY PRODUCTION in EUROPE
The first histogram describes the situation of the renewable energies share of primary energy consumption in the countries of the European Union in 2005. This share is estimated at 6.38%1 vs. an objective of 12% for 2010. European efforts shall have thus permitted a 0.30 point increase with respect to 2004. This increase corresponds to an additional renewable origin primary energy consumption of the order of 5.2 Mtoe out of a total of 112.1 Mtoe.
This increase has taken place in a context where total primary energy consumption for EU countries remained stable with respect to 2004 (in the neighbourhood of 1 756 Mtoe). This last observation is good news for the renewable sectors that too often saw their respective increases over the last few years cancelled out by the growth in total primary energy consumption. The RE share could even have been greater (approx. 6.48%) if 2005 had not been a year that was so marked by a rainfall deficit that significantly slowed down hydraulic production. In this way, the countries where performances declined this year (Latvia, Portugal, Slovenia, Spain, France and Italy) are those where hydropower production represents a significant share of the renewable contribution. On the other hand, in spite of this increase, it's obvious that the rate being followed at present will not make it possible to reach the objective that's set for the European Union countries. The European Commission has also made this same observation and is expecting a 9% share in 2010. Another fact is that the EU situation conceals a wide heterogeneity between the different countries. The member States, as a function of their natural resources (wind, forests, hydraulic, solar and geothermal deposits) and of the economic fabric having developed around each sector, have contrasted implications. It should be noted that the six leading European countries in terms of their share of primary energy of renewable origin have in common the fact that they are all large forestry countries with sizeable hydraulic potentials.1 Including hydropower electricity production of pump-storage installations.

## Slide 16: Development of Renewable Electricity Production in Europe (in %)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: STATE OF RENEWABLE ENERGIES IN EUROPE – 2006 EurObserv'ER
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: 2. RENEWABLE ELECTRICITY PRODUCTION in EUROPE
The second European objective pertains to the renewable energies share in gross electricity consumption.
The objectives of the European directive on renewable origin electricity production (21% of gross renewable origin consumption in 2010) does not take into consideration – as the White Paper does – hydroelectric production coming from pump-storage installations functioning with power grid electricity.
The EU percentage is estimated at 13.97% for 2005, which marks a 0.31 point decline with respect to 2004. The very low level of rainfall in 2005, mentioned in the previous paragraph (the worst year in this context for the last 10 years), is the principal cause of this drop. If hydroelectric production could have been maintained at the level of 2004, which was an average year, the share of renewable electricity would have reached 14.60% in 2005, i.e. + 0.32 points with respect to 2004. The increase was thus the result of development in the other renewable sectors, in particular wind power and biomass.
Four countries were particularly affected by drought in 2005: Portugal (-8.85 points in 2005 with respect to 2004), Spain (-3.47 points), France (-1.81 points) and Italy (-1.78 points). To the contrary, a good hydroelectric year permitted Sweden to markedly increase its share in electricity consumption (+8.50 points). In the short term, these variations can conceal the efforts made by certain countries to develop other renewable sectors. This is especially the case of Spain and the very strong growth in its wind power sector.
Germany should also be cited because it is a country which, in spite of its low hydroelectric potential, is a mainstay of renewable electricity production in Europe and has succeeded in a few years time to raise its share of renewable sectors up to a level very near to that of France. This is the reward for practically ten years of policies in favour of electricity produced from the wind power and biomass sectors. These two energies are also at the origin of the increase in the share of renewable electricity in the Netherlands (1.71 points), Ireland (+1.70 points) and the UK (+0.6 points).
In this way, the decrease in the share of gross renewable electricity consumption recorded in 2005 is not representative of the efforts currently being made by most European countries. Powered by the political will of EU countries to honour their commitments, we can expect to see this ratio on the rise, being pushed upward in the coming years .

## Slide 17: # 4: Environmental Problems: - Global CO2-Challenge: Risks, Emissions, Green House Effect - Local air pollution
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6

## Slide 18: Observed Climate Changes: Surface Temperature, Sea Level and Snow Cover
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: IPCC 2007
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: The warming of the climate system is unequivocal:
Increasing global air and ocean temperatures
Rising global average sea level
Reductions of snow and ice
Extreme events:
The frequency of heavy precipitation events has increased over most areas
From 1900 to 2005, precipitation increased significantly in eastern parts of North and South America, northern Europe and northern and central Asia but declined in the Sahel, the Mediterranean, southern Africa and parts of southern Asia
Globally, the area affected by drought has likely increased since the 1970s
There is now higher confidence than in the TAR in projected patterns of warming and other regional-scale features, including changes in wind patterns, precipitation, and some aspects of extremes and sea ice
Source: IPCC 2007: 27th Session of the Intergovernmental Panel on Climate Change, Valencia 12-17th November 2007
For further background: http://www.ipcc.ch/

## Slide 19: Projected Impacts of Climate Change
Source: Stern 2006
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: Stern 2006 Stern Review on the Economics of Climate Change
For explanations and background info: Stern Report_Summary_of_Conclusions_06.pdf (4 pages, file attached)

## Slide 20: Global warming – millions of people at risk in 2080
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
  The EU has decided on 2ºC as the maximum prudent global warming level

## Slide 21: Current sources of greenhouse gas emissions
Source: IEA 2004
B
Notes: Source: IEA World Energy Outlook 2004

## Slide 22: What is a Green House Gas
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Atmospheric gases that cause global warming and climate change
Major: carbon dioxide (CO2), methane (CH4) and nitrous oxide (N20)
Less prevalent --but powerful -- hydrofluorocarbons (HFCs), perfluorocarbons (PFCs) and sulphur hexafluoride (SF6)
Source: UNFCC
www.eo.ucar.edu/kids/green/warming4.htm
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: For background see next slide

## Slide 23: What is the Greenhouse Gas Effect?
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: UNFCC 2006
B
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
The Greenhouse Effect: Essentially, all energy that enters the Earth’s atmosphere comes from the sun. The incoming radiation is partly absorbed, partly scattered, and partly reflected back into space by the various gases of the atmosphere, clouds, and aerosols — tiny particles suspended in the atmosphere. The sun emits solar radiation mainly in the form of visible and ultraviolet radiation. As this radiation travels towards the Earth, approximately 25% of it is absorbed by the atmosphere and 25% is reflected by the clouds back into space. The remaining radiation travels to the Earth and heats its surface. Because the Earth is much cooler than the sun, energy reflected from the Earth’s surface is lower in intensity than that emitted from the sun, i.e. in the form of invisible infrared radiation. About 90% of the infrared radiation reflected by the earth’s surface is absorbed by atmospheric trace gases, also known as “greenhouse gases,” before it can escape to space. These gases, as well as clouds, re-emit this radiation — sending it back toward ground. The atmosphere acts like the glass in a greenhouse,
allowing short-wavelength radiation to travel through, but trapping some of the long wavelength infrared radiation which is trying to escape. This process makes the temperature of the atmosphere rise just as it does in the greenhouse. This is the Earth’s natural greenhouse effect and keeps our planet about 60ºF warmer than it might otherwise be.
(Courtesy: National Oceanic and Atmospheric Administration)
<number>

## Slide 24: GHG atmospheric lifetimes and human sources
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: http://vitalgraphics.net/graphic.cfm?filename=climate2/large/9.jpg
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
<number>

## Slide 25: Technology Options for CO2-Reduction - Illustration of the Scale of the Task
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: ExxonMobil on 22 October 2004
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Table 2 illustrates the scale of the task by citing several massive activities whose implementation could achieve reductions of 3.3 billion tonnes of CO2 emissions (or 1 gigatonne of carbon).
For example, one could install 150 times the current wind power capacity, bring into operation 1 billion hydrogen cars to replace conventional 30 (US) miles per gallon (7.84 litres per 100 kms) cars or install five times the current nuclear capacity. Alternatively, one could use half of the US agricultural area for biomass production.

## Slide 26: Local air pollution problems related to the use of fossil fuels
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Acidification
Photochemical smog
Particulate Matter (PM10)
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 27: Acidification
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Acidification is the process whereby air pollution (mainly ammonia, sulphur dioxide and nitrogen oxides) is converted into acid substances. This “acid rain” causes damage to forests and lakes, and helps release heavy metals into groundwater.
Source: Scottish Environment Protection Agency (www.sepa.org.uk)
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Acidification is the process whereby air pollution (mainly ammonia, sulphur dioxide and nitrogen oxides) is converted into acid substances.
This “acid rain” is best known for the damage it causes to forests and lakes. Less well known are the many ways it damages freshwater and coastal ecosystems, soils and even ancient historical monuments, or the heavy metals these acids help release into groundwater.
Sulphur dioxide and the nitrogen oxides are mainly emitted by burning fossil fuels. The 1990s saw these emissions drop substantially, thanks to a combination of European Directives forcing the installation of desulphurisation systems, the move away from coal as a fossil fuel, and major economic restructuring in the new German Lander.
Acidification is nevertheless still a major environmental problem in Europe. It is a cross-border issue, requiring coordinated initiatives across countries and sectors. For more information on acidification in Europe, see the European Environment Agency website: http://www.eea.europa.eu/themes/acidification

## Slide 28: Photochemical smog
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
It is a type of air pollution produced when sunlight acts upon motor vehicle exhaust gases to form harmful substances such as ozone (O3), aldehydes and peroxyacetylnitrate (PAN).
Source: www.eco.pref.mie.jp
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Photochemical Smog
Photochemical smog is a type of air pollution produced when sunlight acts upon motor vehicle exhaust gases to form harmful substances such as ozone (O3), aldehydes and peroxyacetylnitrate (PAN). Ozone causes breathing difficulties, headaches, fatigue and can aggrevate respiratory problems. The peroxyacetylnitrate (CH3CO-OO-NO2) in photochemical smog can irritate the eyes, causing them to water and sting.
Ozone Production
Motor vehicles produce exhaust gases containing oxides of nitrogen such as nitrogen dioxide (NO2) and nitric oxide (NO). At the high temperatures of the car's combustion chamber (cylinder), nitrogen and oxygen from the air react to form nitric oxide (NO):
N2(g) + O2(g) -----> 2NO(g)
Some of the nitric oxide (NO) reacts with oxygen to form nitrogen dioxide (NO2):
2NO(g) + O2(g) -----> 2NO2(g)
The mixture of nitric oxide (NO) and nitrogen dioxide (NO2) is sometimes referred to as NOx. When the nitrogen dioxide (NO2) concentration is well above clean air levels and there is plenty of sunlight, then an oxygen atom splits off from the nitrogen dioxide molecule:
sunlight
NO2(g) ----------> NO(g) + O(g)
This oxygen atom (O) can react with oxygen molecules (O2) in the air to form ozone (O3):
O + O2 -----> O3
Nitric oxide can remove ozone by reacting with it to form nitrogen dioxide (NO2) and oxygen (O2):
NO(g) + O3(g) -----> NO2(g) + O2(g)
When the ratio of NO2 to NO is greater than 3, the formation of ozone is the dominant reaction. If the ratio is less than 0.3, then the nitric oxide reaction destroys the ozone at about the same rate as it is formed, keeping the ozone concentration below harmful levels. The reaction of hydrocarbons (unburnt petrol) with nitric oxide and oxygen produce nitrogen dioxide also in the presence of sunlight, increasing the ratio of nitrogen dioxide to nitric oxide.
Peroxyacetylnitrate Production
Nitrogen dioxide (NO2), oxygen (O2) and hydrocarbons (unburnt petrol) react in the presence of sunlight to produce peroxyacetylnitrate (CH3CO-OO-NO2):
Sunlight
NO2(g) + O2(g) + hydrocarbons ----------> CH3CO-OO-NO2(g)
Source: AUS-e-TUTE (ausetute.com.au)

## Slide 29: Particulate matter (PM10)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Particulate matter is the sum of all particles suspended in air, many of which are hazardous.
Such particles vary greatly in size and composition, which influences how human health is affected.
The PM10 (particles measuring 10µm or less) standard was designed to identify those particles likely to be inhaled by humans, and PM10 has become the generally accepted measure of particulate material in the atmosphere in Europe.
The main sources of primary PM10 are road transport (all road transport emits PM10, but diesel vehicles emit a greater mass of particulate per vehicle kilometre), stationary combustion (domestic coal combustion has traditionally been the major source of particulate emissions) and industrial processes (including bulk handling, construction, mining and quarrying)
Source: NAEI (www.naei.org.uk)
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Particulate matter is the sum of all solid and liquid particles suspended in air, many of which are hazardous. This complex mixture contains for instance dust, pollen, soot, smoke, and liquid droplets.
These particles come in many different size ranges such as coarse, fine and ultrafine. They also vary in composition and origin. Particles are either directly emitted into the air by sources such as combustion processes and windblown dust, or formed in the atmosphere by transformation of emitted gases such as SO2. In Europe, sulphate and organic matter are the main components of particulate air pollution in terms of the mass of the particles. Mineral dust, nitrate, and soot can also be major components under certain conditions.
In Europe, long-term exposure to current ambient particulate matter concentrations may affect the lungs of both children and adults and may reduce life expectancy by a few months, mainly in subjects with pre-existing heart and lung diseases. Ambient particulate matter is responsible for harmful effects on health, even in the absence of other air pollutants. Both fine and coarse particles have been shown to affect health, in particular the respiratory system. Fine particles are more dangerous than coarse particles. Apart from the size of the particles, other specific physical, chemical, and biological characteristics that can influence harmful health effects include the presence of metals, PAHs, other organic components, or certain toxins. When particulate matter is combined with other air pollutants, the individual effects of each pollutant are cumulated. In certain cases, especially for combinations of particulate matter with ozone or allergens, effects were shown to be even greater than the sum of the individual effects. When particulate matter interacts with gases, this interaction changes its composition and, therefore, its effects. Certain groups of people are more susceptible to suffer health effects due to ambient particulate matter. These include elderly people, children, people with a pre-existing heart and lung disease, asthmatics, and socially disadvantaged and poorly educated populations. Because some persons are vulnerable even at low concentrations of ambient particular matter, no threshold has been identified below which nobody’s health is affected.
Studies on human populations suggest that a number of sources of particulate matter, especially motor vehicle emissions and coal combustion, are linked to adverse health effects.
Personal exposure depends both on particulate matter levels in ambient outdoor air and on specific indoor sources of particulate matter such as smoking or exposure at work. The impact on public health of long-term exposure to particulate matter is probably larger than that of short-term exposure to peak concentrations. Long-term exposure particularly affects populations living near busy roads.
Source: GreenFacts (www.greenfacts.org)

## Slide 30: Technologies to control local air problems related to fossil fuels
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
End-of-pipe systems on power plants and vehicles
Increase in efficiency of power plants and vehicles
Substitution of fossil fuels for power and transport with cleaner fuels, possibly also carbon-free and renewable
Part 1
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 31: # 5: First Solution: Reduction of Demand before Supply!
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6

## Slide 32: Energy Conservation/Efficiency First! Also for H2-Economy!
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Basic design principle for all energy supply systems:
Step: Reduction of energy demand
Step: Efficient supply of remaining demand
Generally: any design should first of all focus on all possible demand reduction potentials. Afterwards, the remaining demand should be supplied as efficiently as possible. Especially if renewables are involved.
Approach and requirements:
Get good knowledge about the “true” (reduced) demand
This requires good engineering capabilities and more detailed planning – fewer additional security surcharges
System design as opposed to component design
And: Demand depends on information and price: e.g. consumption metering and billing => Introduce demand related billing!
New design philosophy: from „the bigger the better“ to „the more efficient the better”
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Keywords, comments, remarks:
Generally any design approach should first of all focus on energy conservation by evaluating all possible demand reduction opportunities. Only afterwards the remaining demand should be supplied as efficiently as possible - including renewable supply options. This requires an integrated planning concept. Afterwards, the remaining demand should be supplied as efficiently as possible. Especially if scarce ressources like hydrogen or renewables are involved A good example for this approach is the reduction of all electrical and thermal cooling loads including solar shading options before assessing an air conditioning unit.
Engineering fees not only f(investment volume) but on efficiency and life cycle cost

## Slide 33: Reduction Potentials in CO2-related Emissions by sectors and regions
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: IEA WEO `04
Part 1
Part 2
Part 3
Part 4
Part 5
Part 6
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: Center for European Policy Studies (CEPS) 2005: TOWARDS A GLOBAL CLIMATE REGIME. PRIORITY AREAS FOR A COHERENT EU STRATEGY
  Energy efficiency holds the biggest potential to reduce GHG emissions. In the World Alternative Policy Scenario formulated by the IEA in its 2004 World Energy Outlook, more efficient use of energy in a wide range of applications, including vehicles, electric appliances, lighting and industrial uses, accounts for almost 60% of the reduction in CO2 emissions. A shift in the fuel mix for power generation in favour of renewables and nuclear energy power accounts for most of the rest. For the potential reductions identified by the IEA, see Table 3.
  Improved energy efficiency would need to replicate and even reinforce the trends towards higher efficiency that has been achieved throughout the 1970s and 1980s. According to the IEA (2004b), the greatest reductions of CO2 emissions/GDP took place in the 1970s and 1980s, mainly as a result of energy efficiency, which was responsible for about 60% of the total.16 The high energy prices brought on by the oil crises of the 1970s stimulated energy efficiency and the search for new energy sources. Similarly the declining energy savings rate in the 1990s can be explained by lower relative energy prices from 1986 onwards. For example, the energy share of total production costs for industry has fallen by 50%. Similarly, the share of income spent on energy has fallen by 20-50%. And compared to overall disposable income, fuel costs for cars have fallen by 20-60%.

## Slide 34: Global CO2 Mitigation Cost Curve 2030 (beyond business as usual)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: Vattenfall 2007
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: Vattenfall’s Global Climate Impact Abatement Map_07
We have identified the costs for different types of CO2-abatement measures. This has resulted in a marginal abatement cost curve (MAC), where the different measures are ordered from the cheapest to the most expensive ones.
As a result, many demand reduction/efficiency measures have high potentials at negative marginal cost.

## Slide 35: # 6: Hydrogen Economy: Visions, System Components, Benefits and Challenges
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 36: Sketch of a Future (H2-)Energy Economy
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
B
Notes: This slide shows how an integrated energy system of the future including hydrogen might look like:
A variety of renewable energy sources like wind, PV and Hydro
H2 is being used as an energy carrier
combining large and small fuel cells for domestic and decentralised heat and electrical power generation.
Local hydrogen networks could also be used to fuel conventional or fuel cell vehicles.
CO2 is being stored in depleted gas wells (CCS - Carbon Capture&Storage)
For explanations and background info: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003.pdf (35 pages, file attached)
H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 37: The Renewable Hydrogen Economy – a Vision
Road Traffic
Aerospace
Rivers
Oceans
Atmosphere
Ground water
Electricity generation
Heat market
Petrochemistry Hydrogen chemistry
Electrolysis
Demineralization
Electricity generation from solar, wind and hydropower
Liquefaction
Air
Source: Ludwig Jörisson, H2 Training manual, chapter 4
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
I
Notes: Source: Ludwig Jörisson, H2 Training manual, chapter 4
Although today hydrogen is produced mainly from fossil sources, in the future hydrogen can be considered as an energy vector allowing electricity generated from solar and wind energy to enter the fuel market for road transport as well as aerospace applications. Furthermore, hydrogen could be used for peak shaving or seasonal energy storage in the electricity market. Additionally, gasification of biomass can provide an additional source of renewable energy for the production of hydrogen.
Production of hydrogen from renewable energies and its use as a fuel in road traffic could decrease the dependency on mineral oil which currently is the dominant source for the production of fuels. Hydrogen produced from renewable energies could also reduce the emissions of CO2 and classical pollutants (e.g. CO, NOx soot) generated by internal combustion engines running on fossil fuels. Fuel cell powered vehicles fuelled by hydrogen can be considered as completely emission free at the point of use. Decentralized electrolyzers located at filling stations or so called home fuellers could provide an option for implementing the early stages of a hydrogen infrastructure.
It has to be taken into account, however, that the implementation of a “hydrogen economy” as shown above must deal with the following key issues:
  Limited volumetric energy density of hydrogen
  Implementation of a new fuel infrastructure
  Limited efficiency for use of hydrogen as energy storage
Other pathways for the conversion of renewable energies into fuels or the storage of electricity for peak shaving and seasonal energy storage might eventually be easier implemented.
Currently, the conversion of biomass to hydrocarbon fuels (e.g. diesel) or methanol are studied intensively. Furthermore, advances in battery technology might allow the implementation of pure electric road vehicles.

## Slide 38: Use of Hydrogen Today
Hydrogen is an important raw material in chemical industry
    Production of fertilizers
    Petrochemistry (Desulfurization, Hydrocracking)
    Food industry (fat hardening)
    Metallurgical processes (annealing, hardening, sintering)
    semiconductors (doping element)
Hydrogen technology is already existing state of the art. However, not as an energy technology. Hydrogen storage and hydrogen transport are well known:
    1900 industrial use, e.g. gas-welding (This could be considered as the beginning of the hydrogen era!)
    1783-1800 first applications in ballooning
    1898 liquefaction to LH2 by James Dewar
    Use in “town gas”, H2-content approx. 50% - 60%
In a future solar hydrogen economy, hydrogen could be used as Clean fuel, Seasonal energy storage, Trans ocean energy transport, Chemical raw material (“regenerative petrochemistry”)
Source: Ludwig Jörisson, H2 Training manual, chapter 4
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
B
Notes: Source: Ludwig Jörisson, H2 Training manual, chapter 4
At the present, approximately 50 million tons of hydrogen are produced worldwide for a plentitude of applications. Appoximately 31 million ton per year are produced from the conversion of fossil fuel (natural gas, heavy oil). Approximately 19 million ton per year are produced as so called byproduct hydrogen mainly from reforming and petrochemical sources. The chemical and metal industry are using hydrogen for more than 100 years in large quantities with a good safety record.
The most prominent use (~ 50%) is the production of ammonia which later on is mostly converted into fertilizers. About 37% of the hydrogen produced is used in petroleum refining mostly for desulfurization and hydrocracking. Approximately 8% hydrogen is used for the production of methanol, mainly for (MBE) Methyl-tert. ButylEther, a powerful anti-knocking additive to gasoline. However, most of the hydrogen produced is used at the site of production. Only 4% are sold as a technical gas which, to mention only a few examples, is used in the food industry for fat hardening, as an inert gas during metallurgical processes or as a high purity doping gas in the semiconductor industry.
In former times town gas consisting of a mixture of CO and hydrogen was used for public energy service. Today, the use of hydrogen for use in energy technology has almost vanished. Nevertheless, waste and byproduct hydrogen which are not isolated from chemical processes, are also still used to generate process energy.
In the future, hydrogen is considered a viable option to provide clean energy. Hydrogen can be produced from a plentitude of primary energies. Initially, these will be fossil energies such as natural gas or coal. As they become available in large quantities, renewable energies such as surplus electricity from wind- and solar power as well as biomass will be the primary source of energy for hydrogen production.
Hydrogen is an ideal fuel for fuel cells. However, it can also be used in internal combustion engines or gas turbines.

## Slide 39: Hydrogen: Primary Energy Sources, Converters and Applications
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
I
Notes: Source: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003
A sustainable high quality of life is the basic driver for providing a clean, safe, reliable and secure energy supply in Europe. To ensure a competitive economic environment, energy systems must meet the following societal needs at affordable prices:
– Mitigate the effects of climate change; – Reduce toxic pollutants; and – Plan for diminishing reserves of oil.
Failure to meet these needs will have significant negative impacts on:
– the economy; – the environment; and – public health.
Measures should therefore be introduced which promote:
– more efficient use of energy; and – energy supply from a growing proportion of carbon-free sources.
The potential effects of climate change are very serious and most important of all, irreversible. Europe cannot afford to wait before taking remedial action, and it must aim for the ideal – an emissions-free future based on sustainable energy. Electricity and hydrogen together represent one of the most promising ways to achieve this, complemented by fuel cells which provide very efficient energy conversion.
Hydrogen is not a primary energy source like coal and gas. It is an energy carrier. Initially, it will be produced using existing energy systems based on different conventional primary energy carriers and sources. In the longer term, renewable energy sources will become the most important source for the production of hydrogen. Regenerative hydrogen, and hydrogen produced from nuclear sources and fossil-based energy conversion systems with capture, and safe storage (sequestration) of CO2 emissions, are almost completely carbon-free energy pathways.
Producing hydrogen in the large quantities necessary for the transport and stationary power markets could become a barrier to progress beyond the initial demonstration phase. If cost and security of supply are dominant considerations, then coal gasification with CO2 sequestration may be of interest for large parts of Europe. If the political will is to move to renewable energies, then biomass, solar, wind and ocean energy will be more or less viable according to regional geographic and climatic conditions. For example, concentrated solar thermal energy is a potentially affordable and secure option for large-scale hydrogen production, especially for Southern Europe. The wide range of options for sources, converters and applications, shown in Figures 1 and 2, although not exhaustive, illustrates the flexibility of hydrogen and fuel cell energy systems.
Fuel cells will be used in a wide range of products, ranging from very small fuel cells in portable devices such as mobile phones and laptops, through mobile applications like cars, delivery vehicles, buses and ships, to heat and power generators in stationary applications in the domestic and industrial sector. Future energy systems will also include improved conventional energy converters running on hydrogen (e.g. internal combustion engines, Stirling engines, and turbines) as well as other energy carriers (e.g. direct heat and electricity from renewable energy, and bio-fuels for transport).
The benefits of hydrogen and fuel cells are wide ranging, but will not be fully apparent until they are in widespread use. With the use of hydrogen in fuel-cell systems there are very low to zero carbon emissions and no emissions of harmful ambient air substances like nitrogen dioxide, sulphur dioxide or carbon monoxide. Because of their low noise and high power quality, fuel cell systems are ideal for use in hospitals or IT centres, or for mobile applications. They offer high efficiencies which are independent of size. Fuel-cell electric-drive trains can provide a significant reduction in energy consumption and regulated emissions. Fuel cells can also be used as Auxiliary Power Units (APU) in combination with internal combustion engines, or in stationary back-up systems when operated with reformers for on-board conversion of other fuels – saving energy and reducing air pollution, especially in congested urban traffic.
In brief, hydrogen and electricity together represent one of the most promising ways to realise sustainable energy, whilst fuel cells provide the most efficient conversion device for converting hydrogen, and possibly other fuels, into electricity. Hydrogen and fuel cells open the way to integrated “open energy systems” that simultaneously address all of the major energy and environmental challenges, and have the flexibility to adapt to the diverse and intermittent renewable energy sources that will be available in the Europe of 2030.
Continued on next slide
H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 40: Hydrogen: Fuel Cell Technologies, Fuels and Applications
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
I
Notes: Source: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003
(continued from previous slide) Europe should lead in undertaking rational analysis of alternative energy options and in demonstrating the benefits of a transition to a widespread use of hydrogen and fuel cells. They will have to provide cost-effective solutions to the following key challenges – the main drivers for Europe’s future energy systems.
Energy security and supply: Today’s society depends crucially on the uninterrupted availability of affordable fossil fuels which, in future, will be increasingly concentrated in a smaller number of countries – creating the potential for geopolitical and price instability. Hydrogen opens access to a broad range of primary energy sources, including fossil fuels, nuclear energy and, increasingly, renewable energy sources (e.g. wind, solar, ocean, and biomass), as they become more widely available. Thus, the availability and price of hydrogen as a carrier should be more stable than any single energy source. The introduction of hydrogen as an energy carrier, alongside electricity, would enable Europe to exploit resources that are best adapted to regional circumstances.
Hydrogen and electricity also allow flexibility in balancing centralised and decentralised power, based on managed, intelligent grids, and power for remote locations (e.g. island, and mountain sites). Decentralised power is attractive both to ensure power quality to meet specific customer needs, as well as reducing exposure to terrorist attack. The ability to store hydrogen more easily than electricity can help with load levelling and in balancing the intermittent nature of renewable energy sources. Hydrogen is also one of the few energy carriers that enables renewable energy sources to be introduced into transport systems.
Economic competitiveness: Since the first oil crisis in the 1970s, economic growth has not been directly linked with growth in energy demand in the industrial sector, whereas in the transport sector increased mobility still leads to a proportionate increase in energy consumption. The amount of energy needed per unit growth must be reduced, while the development of energy carriers and technologies to ensure low-cost energy supply is of great importance. Development and sales of energy systems are also major components of wealth creation, from automobiles to complete power stations, creating substantial employment and export opportunities, especially to the industrialising nations. European leadership in hydrogen and fuel cells will play a key role in creating high-quality employment opportunities, from strategic R&D to production and craftsmen.
In the US and Japan, hydrogen and fuel cells are considered to be core technologies for the 21st century, important for economic prosperity. There is strong investment and industrial activity in the hydrogen and fuel cell arena in these countries, driving the transition to hydrogen – independently of Europe. If Europe wants to compete and become a leading world player, it must intensify its efforts and create a favourable business development environment.
Air quality and health improvements Improved technology and post-combustion treatments for conventional technologies are continuously reducing pollutant emissions. Nevertheless, oxides of nitrogen and particulates remain a problem in certain areas, while the global trend towards urbanisation emphasises the need for clean energy solutions and improved public transport. Vehicles and stationary power generation fuelled by hydrogen are zero emission devices at the point of use, with consequential local air quality benefits.
Greenhouse gas reduction: Hydrogen can be produced from carbon-free or carbon-neutral energy sources or from fossil fuels with CO2 capture and storage (sequestration). Thus, the use of hydrogen could eventually eliminate greenhouse gas emissions from the energy sector. Fuel cells provide efficient and clean electricity generation from a range of fuels. They can also be sited close to the point of end-use, allowing exploitation of the heat generated in the process.
Greenhouse gas savings of about 140 MtCO2 per year (14% of today’s levels of CO2 emissions from electricity generation) could be achieved if about 17% of the total electricity demand, currently being supplied from centralised power stations, is replaced by more efficient decentralised power stations, incorporating stationary high-temperature fuel-cell systems fuelled by natural gas. Fuel-cell systems will be used as base load in the future decentralised energy systems.
These examples are not proposed as targets, but merely to serve as illustrations of the CO2 savings that could be achieved with quite modest penetrations of hydrogen vehicles and fuel cell-based stationary power generation. Together, 15% regenerative hydrogen vehicles and the above distributed fuel cell/gas turbine hybrid systems could deliver about 250 MtCO2 savings per year. This is approximately 6% of the energy-related CO2 emissions forecast in 2030, and progress such as this would allow Europe to move beyond the Kyoto Protocol.

## Slide 41: Fuel Cell Principle
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
I

## Slide 42: Hydrogen Production Technologies (Summary)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
I
Notes: Source: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003

## Slide 43: Hydrogen Storage Technologies (Summary)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
I
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 44: General Advantages of Fuel Cell Systems
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
  High efficiency.
  Zero emissions when using hydrogen, and very low emissions (e.g. NOx, CO…) when using other fuels.
  Mechanical simplicity, low vibration and noise, low maintenance requirements.
  A high ratio of electricity to heat compared with conventional combined heat and power plants.
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Fuel cells convert fuel and air directly to electricity, heat and water in an electrochemical process. Unlike conventional engines, they do not burn the fuel and run pistons or shafts, and so have fewer efficiency losses, low emissions and no moving parts.
Source: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003

## Slide 45: Benefits of Stationary Fuel Cells
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
  Efficiency: Fuel cells are highly efficient, whatever the size, and have high power quality.
  Emissions: Very low to zero carbon emissions and no emissions of harmful ambient air pollutants such as nitrogen dioxide, sulphur dioxide or carbon monoxide.
  Environment: Low levels of noise and emissions mean fuel cells can be sited in sensitive areas.
  Convenience: Fuel cells can provide both heat and power from a range of fuels; compared to conventional Combined Heat and Power (CHP) systems they operate at a higher power to heat ratio.
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003

## Slide 46: Benefits of Transport Fuel Cells (1/2)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
  Efficiency: Fuel cell cars have demonstrated very high efficiencies when operated with hydrogen, compared both to internal combustion engines and fuel cells coupled with onboard reforming of methanol or gasoline;
  CO2 emissions and energy security: Fuel cell vehicles using hydrogen offer the greatest benefits over internal combustion engines of the future and over fuel cell vehicles using other fuels, especially when viewed in the context of a longer term transition to renewable hydrogen;
  Regulated emissions: Fuel cell cars have very low emissions, and even zero emissions at the point of use when fuelled by hydrogen.
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003
Additional background: (Source: Center for European Policy Studies (CEPS) 19.11.04: The climate change challenge as seen from the EU)
Hydrogen in Transport: In the long-term hydrogen has considerable promises and may become the fuel for the transport sector able to meet necessary volumes and environmental standards. However given that fossil fuels will be the main source for hydrogen in the next decades[i] this has little value without separation and storage of CO2 from hydrogen production.
To date hydrogen in transport faces three basic challenges. The first is to develop the infrastructure, the second the availability and cost-effectiveness of the vehicle technology and the third regulatory standards for safety. There is still controversy on whether the infrastructure or vehicle challenge is more difficult.[ii] Both needs considerable technology focus and investment to deliver the necessary breakthrough, most likely over decades.
[i] production costs for hydrogen from using electricity for electrolysis of water will not be competitive with for example natural gas reforming.
[ii] The alternative fuels group organised by DG TREN of the European Commission concluded that vehicle technology is the principal challenge.
Hydrogen and fuel cell vehicles offer great promise for addressing GHG emissions in the longterm. In the short and mid-term, however, there is scope for technological improvement in existing conventional technologies, such as the internal combustion engine, in a cost-effective way. Forecasts give a potential for specific fuel consumption reduction for vehicles with direct drive until 2030 of around 20%, compared to current diesel vehicles. Internal combustion engines typically convert 15% of the energy content of fuels into useful mechanical work. Even small improvements in engine efficiency from 15% to 20% can therefore make a large impact on energy demand (see WBCSD, 2004a). The use of hybrid technology can also contribute to substantial reductions in CO2 emissions. Combined with advanced aerodynamics, lightweight materials, the reduction of rolling resistance (including low rolling resistance tires) and high efficiency engines, there is further scope for increased efficiency.
It is possible that hydrogen (H2) will be the preferred energy carrier for the road transport sector in the long-term, capable of meeting necessary volumes and environmental standards. However, fossil fuels will be the main source for hydrogen in the next decades – given the fact that the costs for producing hydrogen via electrolysis of water will not be competitive for example with natural gas reforming. Therefore, until we master carbon capture and storage, hydrogen has little value for reducing GHG emissions. And even after technological breakthroughs are achieved, hydrogen faces two basic challenges. The first concerns the development of infrastructure; the second is the vehicle technology. There is still controversy over which of these two challenges is the more difficult to overcome when considering the potential for large-scale use of hydrogen.

## Slide 47: Benefits of Transport Fuel Cells (2/2)
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
  Power: Fuel cells can provide on-board electricity with high efficiency. Fuel cell cars could produce (back-up) power for homes, offices, or remote locations;
  Performance and convenience: Hydrogen and fuel cell vehicles could provide similar or improved qualities in terms of performance and convenience.
  Congestion: Silent vehicles could deliver goods at night, taking traffic off roads during the day.
  Comfort: Fuel cell vehicles have a very smooth, refined ride and emit low noise.
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: EC_Hydrogen Energy and Fuel Cells. A vision of our Future_2003

## Slide 48: Broad classification of GHG mitigation options => H2 is least cost effective!
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
Source: CEPS 2006
Source: Center for European Policy Studies (CEPS) 2006
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
A
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>
Source: Center for European Policy Studies (CEPS) 2006: REVISITING EU POLICY OPTIONS FOR TACKLING CLIMATE CHANGE. A SOCIAL COST-BENEFIT ANALYSIS OF GHG EMISSIONS REDUCTION STRATEGIES
This graph offers a good chance to controversially discuss the role of Hydrogen with regard to GHG mitigation in relation to other energy carriers such as CHP, biofuels or nuclear as well as energy efficiency measures such as insulation or heating efficiency. Off course, with further technology developments classifications within the grah may change.
From the perspective of a social cost-benefit analysis, five options stand out as offering the best cost-benefit ratio when taking externalities into account, at least those that can be quantified:
  • Insulation is highly cost-effective from the end-user point of view in reducing the emissions of GHGs and has some ancillary benefits for energy security and air quality, although the overall scale for achieving reductions is only medium if compared to supply side options.
  • Integrated gasification combined cycle (IGCC) power plants have medium costs but contribute significantly to the (probable) long-term goal of applying carbon capture and storage (CCS) in such and other coal-fired plants.
  • Bio-fuels for transportation have medium to high implementation costs and high benefits for energy security, but there may be scale limitations.
  • The cost of combined heat and power (CHP) is probably low (with high uncertainty), while having both a large potential to reduce emissions of GHGs, and medium ancillary energy supply security and air pollution benefits.
  • Nuclear power appears to be cost-effective and has significant benefits regarding avoided air pollution and energy supply security. Yet its suitability needs to be assessed based on political acceptability and proliferation risks, and including all the costs, such as the cost of the final storage of used fuel and the risk of accidents.
Future development of hydrogen fuel cells is very uncertain and depends on different drivers, including energy prices, technology development and climate policy. For CO2 reduction calculations, this option interacts with biofuels, hybrid vehicles and fuel efficiency improvements. The development of CCS furthermore is important since it creates the possibility to produce hydrogen in a climate-friendly and cost-effective fashion.

## Slide 49: Future Challenges for Fuel Cells
© Graz Energy Agency - For requests: Bleyl@grazer-ea.at
  Cost: Except in premium applications such as back-up power generation for major financial institutions, fuel cells are generally today too expensive for commercial introduction.
  Lifetime: Some fuel cell systems have been demonstrated for thousands of hours, but the majority must still be proven.
  Reliability: Not only fuel cells, but also supporting equipment such as fuel processors, must be proven.
  Novelty: In most conservative markets, any new technology requires significant support and public understanding in order to compete.
  Technological breakthroughs are needed for simultaneously improving fuel cell performance, reliability and cost.
  Infrastructure: Refuelling, large-scale manufacturing processes and support infrastructures, such as trained personnel, are not yet available for fuel cell systems.
Source: EC DGRD 2003
Part 1
Part 2
Part 3
Part 4
Part 6
Part 5
B
Notes: H2 Training Manual
29.07.26
© ... - For requests: email@email.com
Page <number>