## Slide 1: H2 Training Manual Chapter: Alternative Fuels
Natural Gas, Biofuels, Synthetic Fuels (Hydrogen outlined in a separate chapter)

## Slide 2: “Alternative” Fuels in History - Examples
Fischer-Tropsch- diesel (from Coal):
First industrial production in 1934 in Germany -> very important during World War 2.
Bio-ethanol (from potatoes or sugar beets):
First usage in prototype of combustion engine of Mr. Nikolaus A. Otto in 1860.
1925 in Germany for “World” War 2.
Since 1970 in Brazil and USA.
Vegetable oil (from rape, sunflowers …)
Since oil crisis 1970s research actions and usage.

## Slide 3: Content
Actual situation: worldwide and EU.
Definitions:
    Alternative fuels vs. biofuels.
    1st and 2nd generation fuels.
Overview and description of alternative fuels
    Production and origin.
    Applicability.
    Ecological aspects.
    Examples.
Outlook
    R&D, political, food vs. fuel discussion.

## Slide 4: Actual situation - worldwide
Alternative fuels only play a small role in the transport sector.
  Fuels from crude oil supply 96% of worldwide energy demand for transportation. Other forms only have a significant role at a local level or for specific transport applications.
  Dependence on crude oil is not ideal.
      diversification of primary energies is necessary.
Biofuels production 33 compared to 1,200 billion litres of gasoline produced in 2004 worldwide (< 3%).
  Ethanol: Brazil and USA world’s leader in production and consumption.
  Biodiesel: 2 billion litres world production, more than 90% in EU25 especially in Germany.
Source: Biofuels Research Advisory Council: Biofuels in the European Union. 2006.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B
Notes: Alternative fuels only play a small role in the transport sector. In other sectors AF are not significant and only some first practice plants are realised (e.g. vegetable oil in CHP plants or biogas feed in the gas network).
  Fuels from crude oil supply 96% of worldwide energy demand for transportation. Other forms of energy (coal, natural gas, alcohols, electric energy) only have a significant role at a local level or for specific transport applications.
  Dependence on crude oil is not ideal
    most important reserves in politically unstable regions
    fluctuating crude oil prices
    economic uncertainty
        diversification of primary energies is necessary
Biofuels production of 33 billion litres in 2004 is small compared to 1,200 billion litres of gasoline produced annually worldwide. Currently the most important biofuels are the liquide biofuels ethanol and biodiesel. Brazil has been the world’s leader (and primary user) of fuel ethanol for more than 25 years, producing slightly less than half the world’s total in 2004. All fuelling stations in Brazil sell pure (95%) ethanol (E95) and gasohol, a 25% ethanol/75% gasoline blend (E25). The US is the world’s second-largest consumer and producer of fuel ethanol. The growth of the US market is a relatively recent trend; ethanol production capacity increased from 4 billion litres in 1996 to 14 billion litres in 2004. Other countries producing and using fuel ethanol include Australia, Canada, China, Columbia, Dominican Republic, France, Germany, India, Jamaica, Malawi, Poland, South Africa, Spain, Sweden, Thailand, and Zambia.
Total world production of biodiesel in 2004 was more than 2 billion litres, of which more than 90% was produced in the EU25. Growth has been most marked in Germany where pure biodiesel (B100) in Germany enjoys a 100% fuel-tax exemption, and the country now has over 1 500 fuelling stations selling B100. Other biodiesel producers and users are France and Italy, with lesser amounts produced and used in Austria, Belgium, Czech Republic, Denmark, Indonesia, Malaysia, and the United States.

## Slide 5: Actual situation - EU
Source: Biofuels Research Advisory Council: Biofuels in the European Union. 2006.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B
Notes: The figure above shows the growth in biofuel production in the EU since 1993. Liquid biofuels in the EU 25 amounted to 2040 ktoe in 2004 or about 0.7% of the market. Notwithstanding the significant growth, the self-imposed 2005 reference values of the EU will not be achieved. There is a substantial variation in Member States’ efforts and if all Member States achieve the targets the share will attain only 1.4% in total. Other transport fuels are developed at currently low market volumes, e.g. biogas in Sweden or pure vegetable oil in Germany.

## Slide 6: Actual situation - EU
EU transport sector accounts for > 30% of total energy consumption:
  98% of transport energy consumption depends on fossil fuels.
  One of the main reasons for failing Kyoto targets.
  EU target for 2010 = 5.75% or 18 Mtoe biofuels, this means between 4 and 13% of total agricultural land needed for production.
Liquid biofuels in the EU 25 amounted to 2,040 ktoe in 2004 (0.7% of the market):
  Biodiesel from rapeseed predominates with 2 Mt, mainly in Germany, France and Italy.
  Ethanol mainly produced from wheat in France, Spain and Sweden, with almost 500 000 t.
  Biodiesel and ethanol mainly blended with diesel or gasoline, in low proportions, but high proportion blends ethanol is used for adapted vehicles (Flexi fuel), and pure forms are also sometimes available. Most ethanol is processed into ethyl tertiary butyl ether (ETBE) as an additive to gasoline.
  Other alternative fuels are developed at currently low market volumes, e.g. biogas in Sweden or pure vegetable oil in Germany.
Source: Biofuels Research Advisory Council: Biofuels in the European Union. 2006.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B
Notes: The EU transport sector accounts for more than 30% of the total energy consumption in the Community. It is 98% dependent on fossil fuels with a high share of imports and thus extremely vulnerable to any market disturbance. The growing transport sector is considered to be one of the main reasons for the EU failing to meet the Kyoto targets. It is expected that 90% of the increase of CO2 emissions between 1990 and 2010 will be attributable to transport.
The current production of liquid biofuels in the EU 25 is about 2 Mtoe, which is less than 1% of the market. Although there have been marked increases in production and use in recent years, the market share is to be significantly below the EU policy target for 2010 of 18 Mtoe used in the transport sector.
The EU has a significant potential for the production of biofuels. It is estimated that between 4 and 13% of the total agricultural land in the EU would be needed to produce the amount of biofuels to reach the level of liquid fossil fuel replacement required for the transport sector in the Directive 2003/30/EC. Furthermore, biofuels can contribute to the EU’s objectives of securing the EU fuel supply while improving the greenhouse gas balance and fostering the development of a competitive European (biofuels and other) industry.
Liquid biofuels in the EU 25 amounted to 2040 ktoe in 2004 or about 0.7% of the market.
  Biodiesel from rapeseed predominates with a production of almost 2 Mt in 2004, mainly in Germany, France and Italy.
  Ethanol is mainly produced from wheat, and to a lesser extent sugar beet, in France, Spain and Sweden, with a total of almost 500 000 tonnes in 2004.
  Biodiesel and ethanol are mainly used blended with diesel or gasoline, respectively, in low proportions, but high proportion blends, e.g. ethanol used for adapted vehicles (Flexi fuel), and pure forms are also available in some countries. Most ethanol is processed into ethyl tertiary butyl ether (ETBE) as an additive to gasoline.
  Other transport fuels are developed at currently low market volumes, e.g. biogas in Sweden or pure vegetable oil in Germany.

## Slide 7: Definitions: Alternative fuels vs biofuels, 1st and 2nd generation
Alternative fuels vs biofuels:
  Alternative fuels imply any materials or substances that can be used as a fuel, other than conventional fuels, and does not necessarily refer to renewable energy sources.
  Biofuels means liquid or gaseous fuel produced from biomass (biodegradable substances).
1st and 2nd generation of fuels
  1st generation are “conventional” fuels created by e.g. extraction, fermentation, esterification or digestion, such as vegetable oil, biodiesel, bioethanol or upgraded biogas.
  2nd generation fuels are created by thermochemical conversion (e.g. gasification, synthesis), such as hydrogen, methanol, ethanol, DME or BTL diesel .
Sources: Biofuels Research Advisory Council: Biofuels in the European Union. 2006.
en.wikipedia.org: Alternative Fuel. 2007.
www.greencarcongress.com: Secound Generation Biofuels. 2007.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B
Notes: Alternative fuels vs biofuels
    In the context of petroleum substitutes, the term 'alternative fuel' imply any available fuel or energy source, and does not necessarily refer to a source of renewable energy. Alternative Fuels, also known as non-conventional fuels, are any materials or substances that can be used as a fuel, other than conventional fuels. Conventional fuels include: fossil fuels (petroleum (oil), coal, propane, and natural gas), and also in some instances nuclear materials such as uranium. Some well known alternative fuels include biodiesel, ethanol, butanol, chemically stored electricity (batteries and fuel cells), hydrogen, methane, natural gas, vegetable oil, biomass, and peanut oil.
    Biofuels means liquid or gaseous fuel produced from biomass, which means the biodegradable fraction of products, waste and residues from agriculture (including vegetal and animal substances), forestry and related industries, as well as the biodegradable fraction of industrial and municipal waste
1st and 2nd generation of fuels
    1st generation fuels are “conventional” fuels created by e.g. extraction, fermentation or esterification, such as vegetable oil, biodiesel, bioethanol or upgraded biogas
    2nd generation fuels are created by thermochemical conversion (e.g. gasification, synthesis), such as hydrogen, methanol, ethanol, DME dimethyl-ether, SNG or BTL diesel (which is chemically different than the methyl-ester biodiesel produced, for example, from rapeseed or soybeans)
From the policy-maker’s point of view, second-generation biofuels offer a number of advantages:
  They allow the use of a much wider range of raw material, especially waste. This can significantly lower the cost of the feedstock.
  The resulting fuels are high-quality and clean-burning, with potentially a much lower well-to-wheels CO2 profile than other liquid fuel options.
  The cultivation process (if any) could be less environmentally intensive than for ordinary agricultural crops. Lower intensity of cultivation will result in even lower greenhouse gas emissions from cultivation.
Gasification and the subsequent catalytic Fischer-Tropsch processing are key technologies for producing second generation automotive biofuels. That combination of technologies, with its range of different systems and choices, however, makes the development of economically and environmentally viable systems much more complex than, say, building an ethanol plant.

## Slide 8: Overview alternative fuels
Natural gas:
  CNG – compressed natural gas.
  LNG – liquefied natural gas.
Biofuels:
  Biogas (also upgraded).
  Pure Vegetable Oil.
  Biodiesel.
  Bioethanol (also from lignocellulosic).
Synthetic Fuels:
  GTL, BTL, SNG, FT-diesel, (Bio-)Methanol, MTBE, DME.
HTU – hydro thermal transformation.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 9: Natural gas – compressed and liquefied
Production and origin:
  Extracted from ground drills.
  Natural gas consists of > 98% methane.
  Energy content: 1 Nm³ natural gas = 1.16 l petrol.
  Compressed gas: for storage > 200 bar, in pipelines < 100 bar.
  Liquefied gas: liquefaction < - 162 °C .
Applicability (1):
  CNG is presently used in industry, in CHPs or in power plants for heat and power production.
  CNG as vehicle fuel is an alternative: usage in petrol-engines with technical adaptations of the tank, vehicles from nearly all producers available (monovalent or bivalent) .
Sources: Joanneum Research: Treibstoffe der Zukunft. 2005. Umweltschutz 5/2007: Flüssigerdgas.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 10: Natural gas – example Mercedes E200

## Slide 11: Natural gas – compressed and liquefied
Applicability (2):
  LNG: liquefaction = high technical and economical effort.
      only large scale liquefaction and storage plants practical.
      only for transportation purposes instead of CNG pipelines.
Ecological aspects (only CNG).
  15 – 20% less GHG emissions instead of petrol; extraction and transportation losses must be taken into account.
  less CO, SO2, unburnt fuel and particle emissions.
Examples (only CNG):
  Italy, Germany: currently many vehicles in operation.
  CNG fuelling station network necessary.
  LNG liquefaction and transport ships necessary.
Sources: Joanneum Research: Treibstoffe der Zukunft. 2005. Umweltschutz 5/2007: Flüssigerdgas.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 12: Fueling station
Source: Pictures from Energie Steiermark, Steirische Gas und Wärme.

## Slide 13: Biogas
Production and origin:
  Methane gas produced from organic substances containing water by fermentation under anaerobic conditions.
  Produced from agricultural waste, maize and organic waste from industry, households and waste water.
  2 – 3 kg maize silage => 1 Nm³ biogas.
  Energy content: 1 Nm³ biogas = 0.65 Nm³ natural gas.
  Biogas: 60% methane, 40% CO2, ~ 6.6 kWh/Nm³ upgraded biogas: 98% methane, 2% CO2, ~ 11 kWh/Nm³.
  By-products: residues as fertilizer or for improvement of land.
Applicability (1)
  Presently biogas is used in peripheral CHPs.
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 14: Biogas – example Biogas CHP-plant
Source: Pictures GE Jenbacher, Austria.

## Slide 15: Cogeneration Principle CHP = combined heat and power
CHP plant could be:
Engine/Generator.
Gas turbine/Generator.
Steam turbine/Generator.
Fuel Cell.
Source: Bundesverband Kraft Wärme Kopplung, Germany.

## Slide 16: Biogas
Applicability (2):
  Usage of upgraded biogas in petrol-engines with technical adaptations of the tank, vehicles from nearly all producers available.
  Upgraded biogas can be blended with natural gas, currently few plants to feed in the natural gas grid installed.
  Distribution infrastructure of natural gas can be used, only few fuelling stations available.
Ecological aspects
  60 – 100% less GHG emissions instead of petrol.
  Avoiding of methane emissions from unfermented waste.
  Little particle emissions.
Examples
  Switzerland, Sweden: presently usage in vehicles (e.g. busses).
  Fuelling station network and feed-in plants necessary.
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 17: Pure Biogas as fuel for Busses in Sweden
Source: Petersson, Swedisch Gas Center, Sweden.

## Slide 18: Refueling of “Biogas” after upgrading and grid injection in Sweden
Source: Petersson, Swedisch Gas Center, Sweden.

## Slide 19: Raw material for a liquid fuel? Yes, sun flowers!

## Slide 20: Vegetable Oil
Production and origin:
  crude or refined oil from oil plants through pressing or extraction, but chemically unmodified.
  produced from oilseeds from rape, sun flowers, false flax.
  3 kg oilseeds => 1 l oil.
  agricultural land: 3 – 4 t oilseeds per ha yearly.
  energy content: 1 l vegetable oil = 0.92 l diesel.
  by-products: plant residues (pomace) as feed or fertilizer.
Applicability (1)
  usage in diesel-engines is possible with technical adaptations (“Elsbett principle”).
  reliability and durability of engines must be improved for a serial production.
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 21
..
Source: Left picture Biotrieb, Austria.

## Slide 22: Vegetable Oil
Applicability (2):
  mixing with (bio)diesel not possible.
  distribution infrastructure is not complex and mainly existent.
  oil preheating necessary in the case of low outdoor temperatures because of its viscosity.
Ecological aspects:
  50% less GHG emissions instead of diesel.
  free of sulphur and heavy metals.
  Biodegradable.
  much higher mutagenicity (changing of genetic material - causes cancer) in comparison to diesel and biodiesel.
Examples:
  presently usage in CHPs, passenger cars and agricultural machines, e.g. in Germany and Austria.
  fleet tests in procedure (e.g. Austria).
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 23: Rape as raw material for Biodiesel
Source: Picture Münzer Holding, Biodiesel Vienna, Austria.

## Slide 24: Biodiesel
Production and origin:
  a methyl-ester of diesel quality produced from vegetable oil or animal fats.
  oil produced from rape, sun flowers, false flax or edible oil.
  energy content: 1 l biodiesel = 0.92 l diesel.
  production costs incl. refinery: biodiesel 0,55 – 0,6 €/l vs fossil 0,3 – 0,4 €/l
Sources: Joanneum Research: Treibstoffe der Zukunft. 2005. National Biodiesel Board: Biodiesel Production. Ewald Münzer. Vorstandsmitglied ARGE flüssige Biokraftstoffe Österreich.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 25: Biodiesel Vienna – a production plant
Source: Picture Münzer Holding, Biodiesel Vienna, Austria.
Production capacity after enlargement: ~ 340.000 t/a meaning ~ 3 % of total Austrian liquide fuel demand

## Slide 26: Biodiesel
Applicability:
  Mixing with fossil diesel is possible in every proportion.
  Usage in diesel-engines is possible with some technical adaptations.
      blends with fossil-diesel up to 1:1 approved by many car producers.
      blends up to 25% fossil with 85% biodiesel “B85” approved by some car producers, e.g. Volvo or BMW.
      currently only few vehicles approved for pure biodiesel “B100” usage, especially freight vehicles.
  Reliability and durability of engines must be improved for a serial production.
  Distribution infrastructure is similar to that from fossil diesel.
Sources: Joanneum Research: Treibstoffe der Zukunft. 2005.
Ewald Münzer. Vorstandsmitglied ARGE flüssige Biokraftstoffe Österreich.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 27: Biodiesel
Ecological aspects:
  60 – 95% less GHG emissions instead of diesel.
  Less CO and particle emissions, but more N emissions.
  Biodegradable.
Examples:
  Presently blended by 5.75% with fossil diesel all over EU.
  Austrian government plans to blend fossil diesel with 10% biodiesel “B10” as an obligation in 2010 all over the country.
  Examples of passenger cars and trucks running with 100% biodiesel B100 (e.g. bus fleet in Austria, serial vehicles).
      www.ufop.de (only German)
Sources: Joanneum Research: Treibstoffe der Zukunft. 2005.
Ewald Münzer. Vorstandsmitglied ARGE flüssige Biokraftstoffe Österreich.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 28: Bioethanol
Production and origin:
  Produced by fermentation and distillation of biomass (field crops).
  Produced from sugary/starchy field crops like sugar beets, corn, maize or potatos; in future also from linocellulosic.
  2 – 8 kg crops => 1 l bioethanol.
  ½ l Bioethanol => 1 l Bio-ETBE ethyl-tert- butyl-ether (as additive for petroleum).
  Energy content: 1 l bioethanol = 0.68 l petrol.
  High amounts of by-products: mash used as feed, fertilizer or combustible.
  Bioethanol ≈ biobutanol, other prod. process + better attributes.
Applicability (1):
  Usage in petrol-engines is possible with technical adaptations, some vehicles approved by the producers, e.g. Saab Biopower.
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 29: Bioethanol – production plant in Austria
Source: Bioethanol-Anlage Pischelsdorf, Agrana, Austria.
Production capacity: ~ 190.000 t/a meaning ~ 2 % of total Austrian liquide fuel demand

## Slide 30: Bioethanol
Applicability (2):
  Mixing with fossil petrol is possible in every proportion, e.g. E5 (5% bioethanol/95% petrol) and E85 (85% bioethanol).
  Distribution infrastructure is similar to that from fossil petrol.
  Surplus of petrol-products in Europe currently.
Ecological aspects:
  30 – 75% less GHG emissions instead of petrol.
  Higher octane number, less CO and N emissions.
  Biodegradable.
Examples:
  Presently usage in different vehicles (FFV – flexi fuel vehicle).
  Main producers are Brasil, USA, France, Sweden, Spain and Germany  www.superethanol.at (only German).
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 31: Synthetic fuels
Production and origin (1)
  Synthetic fuels are liquid or gaseous fuels (hydrocarbons) obtained from natural gas, oil, coal, biomass or others like waste, oil shale or tar sand.
  First gasification: syngas produced from the different substances; it is a mixture of carbon monoxide, dioxide and hydrogen.
  Second synthesis: appropriate procedures different synthetic fuels are produced.
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 32: Synthetic fuels
Production and origin (2):
  different types of fuels depend on substances of origin and production process (named accordingly):
    BTG – biomass to gas (gaseous fuel from biomass).
    BTL – biomass to liquid: (liquid fuel from biomass), e.g. 1 kg wood = 1/3 kg synthetic biofuel .
    SNG – synthetic natural gas (also from biogas).
    FT-diesel – Fischer-Tropsch- diesel (from coal, gas or wood by certain process).
    Bio-DME – Biodimethylether .
    Biomethanol (energy content 1l = 0.5l petrol), also source material for bio-MTBE methyl-tert-butyl-ether (as additive for petroleum).
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 33: Fischer-Tropsch Diesel production plant Güssing, Austria
Source: Biomassenanlage Güssing, Hofbauer, TU-Wien.

## Slide 34: Synthetic fuels
Applicability:
  Currently chemical usage and R&D actions > no large-scale production or usage.
  Mixing with fossil fuels is sometimes possible.
  Usage in common engines, turbines and fuelcells is possible.
  Most of the distribution infrastructure can be used.
Ecological aspects:
  Up to 80% less GHG emissions instead of petrol or diesel.
  Sometimes less particle, unburned hydrocarbon or sulphur emissions.
Examples:
  Presently only some pilot production plants in operation: e.g. Germany, Austria, South Africa, New Zealand, Malaysia.
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 35: HTU – hydro thermal transformation
Production and origin.
  HTU is the degeneration of organic substances in water or methanol by high pressures and temperatures.
  Depending on the procedure a wide range of products can be made from wood, bio-waste, sludge or mash.
  Products like biocrude, different hydrocarbons, methan or hydrogen can be made.
Ecological aspects.
  Up to 80% less GHG emissions instead of petrol or diesel.
Examples
  Currently HTU technology is under R&D, only pilot plants are planned.
Source: Joanneum Research: Treibstoffe der Zukunft. 2005.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 36: Outlook
Research and Development (technology and market).
  Now and in the next future petrol and diesel engines are the most important machines for mobility .
  Currently petrol an diesel engines have improvement potential (fuel reduction and emissions).
  Hybrid technology is state of the art – combination of petrol engines with electrical engines and batteries.
  Today bioethanol and biodiesel are industrial available, future.
      biodiesel pure in freight vehicles, ships (blended in passenger cars).
      bioethanol blended and also pure in passenger cars.
  Biogas and synthetic (bio)fuels (2nd generation fuels) have potentials for the future > R&D actions needed.
      today's potentials are seen as premium fuel products.
Sources: Joanneum Research: Treibstoffe der Zukunft. 2005. Biofuels Research Advisory Council: Biofuels in the European Union. 2006.
Ewald Münzer. Vorstandsmitglied ARGE flüssige Biokraftstoffe Österreich.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B

## Slide 37: Outlook
Political – EU vision.
  New fuels similar or compatible to today‘s fuel types.
  ¼ of transport fuels from biofuels by 2030.
Social aspects – food vs. fuels discussion.
  Discussions are ongoing about a displacement competition on agricultural land between food and energy plants.
      bioethanol: food price increase in South America (Brazil) due to extensive production (growing of sugar beets).
      biodiesel: lower influence on food industry, because raw materials are no foodstuff and obliged crop rotations.
      Price influences of food: population growth, income growth, technological improvements, only little energy prices.
      Decrease of unused agricultural land.
Sources: Joanneum Research: Treibstoffe der Zukunft. 2005. Biofuels Research Advisory Council: Biofuels in the European Union. 2006.
Ewald Münzer. Vorstandsmitglied ARGE flüssige Biokraftstoffe Österreich.
© Graz Energy Agency – For requests: schinnerl@grazer-ea.at
B