## Slide 1: Principles of fluid dynamics
Notes: H2 Training Manual
Page <number>
Chapter 6
Title: Principles of fluid dynamics
Level: Basic, intermediate, advanced
Requisites: Chapter 5
Overall aim: The chapter gives an overview of the technical theories that fuels cells rely upon.
Content
Introduction to fluid mechanics
Introduction to water management
Introduction to heat management
Introduction to control systems
Learning outcomes
The student will be able to
Identify the properties of liquids and gases as used in fuels cells
Identify the parameters critical to successful operation
Understand practical application of theories to real world processes
Methodology
Lectures, group work, discussion
Schedule
Basic: 3 one - hour - units
Intermediate and advanced: 4 one - hour - units

## Slide 2: Fluid mechanics definitions
A fluid is a substance that undergoes continuous deformation when subjected to an external force.
Conventionally divided into:
    Compressible: in working conditions they change the specific volume.
    Uncompressible: in working conditions they do not change the specific volume.
In fuel cell systems, water is considered to be uncompressible, while gases (H2, air, steam) are compressible.
Characteristic quantities:
    Pressure.
    Temperature.
    Flow.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 3: Pressure
General concepts
    Pressure is defined as the ratio between the force exerted and the area on which the force is applied, or from another point of view is the force that a fluid applies on the surface of its recipient.
    Absolute pressure is defined with respect to vacuum.
    Gauge pressure is defined with respect to ambient pressure.
    Differential pressure is the difference between the pressure values of two fluids.
    In the S.I. pressure is measured in Pa = 1 N /m2. In practice, the unit {bar} is often used; the conversion is 1 bar = 105 Pa.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 4: Pressure measurement: Bourdon gauge
The process pressure exerts a force on the Bourdon tube, which communicates the elongation variation to a gear connected with the pointer.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 5: Pressure measurement: electronic strain gauge
The core of the system is the strain gauge, a device which varies its electrical resistance according to elongation.
In the pressure transducer, the strain gauge is placed on a diaphragm which deformation – related to the pressure - is measured.
A strain guage is a a device used to measure deformation: electrical resistance of this device changes when the foil is deformed giving an evaluable signal to a signal conditioning device.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 6: Pressure measurement: a guide to sensor selection
When selecting a pressure tranducer, the following points should be considered:
    Accuracy and precision. Typically, a Bourdon-type gauge has a precision range of 1%F.S. to 0.1%F.S., depending on the instrument class.
    The precision of an electronic gauge is in the same range, but it is strongly temperature-dependent.
    If data recording is an issue, electronic gauges are the only choice.
    Wetted part material should be compatible with the process fluid. Stainless steel AISI 316L is compatible with hydrogen gas.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 7: Temperature measurement: thermocouples (I)
The thermocouple uses the Seebeck effect: an electromotive force originates at the connection point between two different metals (the measuring junction).
The reference junction, kept at ambient temperature, is generally built in the temperature transducer.
Thermocouples are classified according to the metallic alloys of their wires. The most commonly used for near-ambient temperatures is the K-type.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 8: Temperature measurement: thermocouples (II)
Thermocouple color code (country-dependent):
Accuracies:
STANDARD SERIES +/- 1.5°C
SPECIAL SERIES +/- 0.5°C
Proper TC-connectors should be used, to avoid junction mismatch.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 9: Temperature measurement: resistance thermometer
Resistance thermometers are metallic wires, whose electric resistance varies with temperature according to:
R = R0 (1+aT)
Generally, platinum wires are used; Pt100 is the acronym of the most common temperature resistance.
The accuracy is computed as follows:
A-class +/-(0.15°C + 0.002*|T|), T in °C
B-class +/-(0.3°C + 0.005*|T|), T in °C
These sensors are mandatory for highly accurate temperature measurements. For all other needs, thermocouples are enough.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 10: Fluid flow
General concepts
    Volume flow is defined as the volume of gas/liquid that crosses a surface perpendicular to the velocity in the unit time. Measurement unit: m3/s in the S.I.
    Q=[V]/[t] = [S].[v]; SI: {m3 / s}
    Mass flow is defined as the mass of gas/liquid that crosses a surface perpendicular to the velocity in the unit time. Measurement unit: Kg/s in the S.I.
    G=[m]/[t] = [d].[S].[v]; SI: {Kg/s}
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 11: Fluid flow measurement: Venturi meter
The fluid flow gives rise to a pressure drop, which depends on the flow itself. The flow value is calculated from the pressure difference measurement: P2 – P2.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 12: Fluid flow measurement: rotameter
The gas flows from the base inlet to the upper aperture of the rotameter.
The float is lifted upwards until the viscous drag force is in equilibrium with gravity.
They are generally used with low flows, due to high head losses.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 13: Fluid flow measurement: thermal flow meter
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 14: Fluid flow measurement: thermal flow meter
    There are two different configurations: inline and bypass.
    In the inline configuration, the sensor is placed in a narrowing of the tube, resulting in high head losses.
    In the bypass configuration, the sensor is placed in parallel to the main flow: head losses are consequantly reduced. However, in this case the time-response is poorer.
    In the inline configuration (see next slide), the gas is heated by the resistor R1. The heat is convection-transported to the sensor R2. Depending on the gas flow, the temperature at R2 will be different.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 15: Fluid flow principles: Bernoulli‘s theorem
Bernoulli’s equation:
z + P/g ρ + v2 / 2 g = constant
Gravimetric Potential Energy
z = height
Pressure Energy
P = static pressure
ρ = fluid density
Kinetic Energy
v = fluid velocity
The total mechanical energy of the flowing fluid, comprising the energy associated with fluid pressure, the gravitational potential energy of elevation, and the kinetic energy of fluid motion, remains constant.
Bernoulli's theorem is the principle of energy conservation for ideal fluids in steady, or streamline, flow.
g is the gravity accelaration constant [L / t2]
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 16: Bernoulli Theorem: Example of application
z = constant
Compressed liquid in the pipe
Low pressure/high speed liquid at the shower outlet
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 17: Fluid flow principles: laminar/turbulent flow
    Laminar flow: the fluid streamlines flows along parallel layers.
    Turbulent flow: the fluid streamlines are wrapped in vortexes.
Turbulent flow
Laminar flow
Navier-Stokes equations describe the motion of a fluid.
Navier-Stokes are non-linear partial differential equations, with no general solution. Computational techinque must be used to solve the system.
A
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 18: Fluid flow principles: laminar/turbulent flow
    Transition from laminar to turbulent flow is related by an adimensional number: Reynolds number, Re.
    Re = ρ v L / μ; where ρ = density, μ = viscosity, v = velocity, L = pipe diameter.
    If Re < 2000, the flow is laminar, for higher Re the flow becomes turbulent.
    H2 flow inside the fuel cell channels is laminar, as well as water flow in the cooling channels.
A
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 19: Laminar flow in channels
Velocity profile inside a cylindrical channel:
Flow VS pressure drop (Poiseuille formula):
Q = volume flow
r = pipe radius
μ = dynamic viscosity
L = pipe length
ΔP = pressure drop
A
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 20: Water management
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 21: Water transport inside the FC
    Water is produced inside the fuel cell due to the overall reaction:
    2H2 + O2 → 2H2O
    The polymeric membrane is proton-conducting only if it is well-humidified -> the water shouldn‘t be completely removed!
    On the other hand, if water-removal rate isn‘t high enough, the cathode floods.
    Water is generally expelled to the atmosphere at the cathode side.
    Sometimes, water can happen to accumulate also at the anode, due to membrane transport.
    Water at anode is generally removed using two different strategies: dead-end or recirculation.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 22: Dead-end VS recirculating anode
Dead-end configuration is generally used for low-power applications.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 23: Humidification of reactant gases
    Even if water is produced by the cell reaction, both fuel and oxidant should be humidified.
    The simplest way to achieve the desired humidity content is using an equilibrium- stage humidifier.
    This technique is however limited to test stations, since it results in heavy and bulky humidifiers.
    In applications, humidity exchangers are generally used.
    the humidity exchanger is a practical solution which allows to use the saturated exhaust cathode gas to humidify the fuel.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 24: Tube-shell water exchangers
courtesy of: Permapure LLC
Humid gas inlet
Humid gas outlet
Dry gas
Flows through
Nafion membrane
    The paths of “humid” and “dry” gases can be exchanged.
    Liquid water can be used instead of humid gas.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 25: Water transport through Nafion
courtesy of: Permapure LLC
    Nafion is a fluorinated polymer which absorbs water.
    Reaction is very fast.
    At saturation, Nafion membrane weight increases by 22% .
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 26: Heat management
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 27: Heat production & transport
    Efficiency of fuel cells stack in operating conditions is around 50%.
    It means that heat production rate equals electric power.
    (1kW electricity -> 1kW heat)
    For small fuel cells (less than 300W), air cooling is enough.
    For larger stacks, water cooling is necessary.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 28: Heat production & transport
    Cooling channels topology is in general patented.
    As a general consideration, they are composed of two segments: “feeding“ and “cooling” channels.
    Cooling channels distribute water on the overall bipolar plate surface; they are narrow and cause the bigger amount of pressure drop in the water circuit.
    Feeding channels are much larger, and distribute water among the cooling channels.
    Demineralised water must be used, otherwise the different plates would be in electrical contact.
    The generated heat is dissipated via a water/air heat exchanger.
    The latter exchanger should be properly chosen to avoid demi-water induced corrosion.
    In any case, a resin filter is generally used to lower the ion content of the cooling fluid.
    Recently, FC stacks use glycol as a cooling medium. While giving compatibility problems with polymeric materials inside the stack, this technology solves the corrosion problems which usually happen with metal heat exchangers.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 29: System integration issues: cogeneration
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 30: System integration issues: cogeneration
    The fuel cell stack is sized to meet the heat requirements of the hot water user.
    The excess electric power is sent to the grid.
    The fuel cell water circuit is filled with demineralised water.
    The filling of the boiler is regulated by the water demand of the final user.
    For maintenance puroposes, both heat exchanger should be periodically dis-assembled and cleaned.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 31: System integration issues: small mobility applications
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 32: System integration issues: small mobility applications
    The metal hydride reservoir needs heat to release hydrogen.
    The heat produced by the fuel cell is re-directed to a metal-hydride reservoir, which is heated via a heat exchanger.
    Depending on the characteristics of the system, the power developed could be limited by the heat-transfer through the metal hydride bed.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 33: Pumps
What is a pump?
A pump is a device used to move liquids or slurries. A pump moves liquids from lower pressure to higher pressure, and overcomes this difference in pressure by adding energy to the system.
Gas pumps are generally referred as “compressors”.
Main pump categories:
Positive displacements pumps:
Kinetic.
Open Screw.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 34: Pumps
Reciprocating pumps:
Piston pumps.
Diaphragm pumps.
Rotary pumps:
Gear pumps.
Rotary vane pumps.
Screw pumps.
Fluid Ring.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 35: Compressors
What is a compressor?
A pump is a device used to move a gas from a low pressure zone o an higher pressure zone: the device overcomes this difference in pressure by adding energy to the system.
Main compressor categories:
Positive Displacement (axial, centrifugal).
Continuous flow compressors (rotary, reciprocating).
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 36: Compressors
General principle:
Energy is transferred to the gas phase continuously from the low pressure zone to the high pressure zone.
Two main types:
Centrifugal (axial and radial).
Peripherals (single stage, multiple stage).
Continuous-flow compressors are machines where the flow is continuous, unlike positive displacement machines where the flow is fluctuating. Continuous flow machines are also classified as turbomachines, and are generally smaller in size and produce less vibration than their counterpart positive displacement units.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 37: Compressors
Centrifugal compressors:
The flow in a centrifugal compressor enters the impeller in an axial directions and exits in a radial direction. In a typical centrifugal compressor, the fluid is forced through the impeller by rapidly rotating blades. The velocity of the fluid is converted to pressure, partially in the impeller and partially in the stationary diffuser.
Typically centrifugal compressor are used in the process industry and in the aerospace applications in several kind of configurations: single and multiple stages.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 38: Ejectors
Ejectors are the simplest among all types of pumps and compressors:
They do not have any moving part.
Ejectors are widely used in fuel cells system for anode recirculation.
Based on Bernoulli’s Principle:
Low pressure zone induced by the contraction in B causes a fluid flow in A: this is a conseguence of the conservation of energy principle.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 39: Controls
Fundamentals of Control Systems.
SISO Control Systems.
PID Control Loops.
MIMO Control Systems.
Model Predictive Control Basics.
B
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 40: Fundamentals of Control Systems
Measured Variables and Controlled Variables
A process consists of several measured and controlled variables.
A Control System is a device able to manage the behaviour of a process.
The simplest control system is called SISO:
Single Input – Single Output
1 Measured Var
(Single Input)
1 Controlled Var
(Single Output)
Control
System
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 41: SISO Systems
There are plenty of Single Input – Single Output control systems.
SISO Systems Families:
On-Off Controls.
Proportional Controls.
PID.
On-Off and PID are the most common type of controllers.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 42: PID Controllers
Proportional Integrative and Derivative Controllers
Are quite common and widely used in process control systems.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 43: MIMO Control Systems
Multiple Input – Multiple Output Control System
Measured Vars
Control
System
Controlled Vars
Complex Control Loops may require advanced logic in order the keep the process in stable conditions.
Typical example are axial furnaces where multiple temperature probe should maintain a given profile. Several power controller must be coordinated in a MIMO controller to reach the desired temperature profile.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>

## Slide 44: Model Predictive Control
MPC is an advanced method used in process control where many variables must be controlled together in order to reach a certain target.
MPC controller target is different from the “Set-Point” of SISO and MIMO controllers: typically an MPC target could be to OPTIMIZE a process in order to reduce costs of raw materials or energy.
MPC rely on dynamic models of the process, used to predict the behaviour of the dependent vs independent variables.
I
Notes: H2 Training Manual
30.07.26
© ... - For requests: email@email.com
Page <number>