## Slide 1: Chapter: CHP Plants
Notes: H2 Training Manual
30/07/26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
Chapter 9
Title CHP Plants
Level Basic, intermediate
Requisites none
Overall aim
The chapter gives an overview of the technical and practical aspects of combined heat and power.
Content
1. The Cogeneration Principle
2. Choose the right cogeneration technology
3. Gas turbine
4. Gas engine
5. Heating oil engine
6. Biogas engine
7. Steam turbine
8. Stirling engine
9. Contact
Learning outcomes
The student will be able to
 understand the advantages of CHP
 identify the range of equipment
Methodology Lectures, group work, discussion
Schedule 2 one - hour - units

## Slide 2: Content
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
The Cogeneration Principle.
Choose the right cogeneration technology.
Gas turbine.
Gas engine.
Heating oil engine.
Biogas engine.
Steam turbine.
Stirling engine.
Contact.
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>

## Slide 3: The Cogeneration Principle: Cogeneration vs Separate Production
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: Bundesverband Kraft-Wärme-Kopplung.
COGENchallenge: Pick the right cogeneration technology. 2006.
B
Notes: Most people think of large clouds pouring out of a massive cooling tower when asked for a picture that illustrates the production of electricity. All of us have seen many different power stations where water is used to cool the process and then condensates into the air. Only a few, however, pose the question why we are actually wasting all this energy that has heated up the water and disappears through the chimney and cooling towers?
Cogeneration drastically reduces this waste of energy. By converting the energy close to the consumer of heat and power, it is possible to use most of it. The graph below illustrates this principle: in the upper half, it is shown how much electricity and heat a typical small-scale cogeneration unit produces with a given number of energy input. In this example, the cogeneration unit has an efficiency of 89%. In the case of separate production of heat (in the boiler) and electricity (in the power station) the efficiency is much lower. Far more fuel is needed, because of the high losses in the power station, additional losses in the electricity network and in the boiler.

## Slide 4: The Cogeneration Principle
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: Bundesverband Kraft-Wärme-Kopplung.
COGENchallenge: Pick the right cogeneration technology. 2006.
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
Cogeneration is a principle and not a single technology. In general, cogeneration can be applied in all cases where electricity is produced by thermal combustion (engine, gas turbine or steam turbine) or where chemical energy is used in a fuel cell. The different technologies may be based on fossil or renewable fuels. By exactly analysing the consumption patterns of individual users, cogeneration schemes can be optimised to supply their specific needs.

## Slide 5: Choose the right cogeneration technology
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
  Different technologies available to produce heat and electricity together.
Criteria:
  Customers must use heat close to the CHP-plant to avoid transmission losses.
  CHP-technology must be chosen according to specific heat demand of the customer.
  Cogeneration units must be sized to the size of the customer
  Available energy source.
      table on next page gives an overview.
      description of different technologies afterwards.
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>

## Slide 6: Overview cogeneration technologies
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
"++" means the technology is very suitable. "+" means less suitable. no quotation means it is not suitable to produce this type of heat.
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
different fuel cells existent; no evaluation possible
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
The range of the available technologies is quite wide. You will choose your cogeneration technology according some criteria, specific to your activity and your heat demand. The table below lists the technologies: "++" means the technology is very suitable to produce the heat you need, and "+" means less suitable. No quotation means the technology is not suitable to produce the type of heat you need. For example the Stirling engine is operated at lower temperatures than other engines, so the production of steam or hot air is not suitable. However there are many different types of fuel cells which are operated at different temperature levels and with different fuels, so a evaluation for steam and hot air is not possible (for more information please refer to chapter 5 fuel cell technology).

## Slide 7: Gas turbine
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
  Technology very important for large-scale cogeneration.
  Wide range of units available: starting at microturbines with ~30 kWe.
  Reduced emissions of sulphur or nitrogen compared to oil.
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
Gas turbines have become the most widely used prime mover for large-scale cogeneration in recent years. Gas turbines are not only used in large-scale applications. Smaller units, starting at around 400 kWe are available on the market. Since the late 1990s microturbines have become available. They are derived from automotive turbo-chargers and are available from 30 kWe. Microturbines use less space than conventional engines and maintenance costs are lower. Moreover, the emission of pollutant gases is reduced, especially those gases that cause acid rain and ozone layer depletion. Electrical efficiencies are typically lower than in internal combustion engines.

## Slide 8: Gas turbine - scheme
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: COGENchallenge: Pick the right cogeneration technology. 2006. and Wikipedia. 2007.
compressor
I
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
A gas turbine extracts energy from a flow of hot gas produced by combustion of gas or fuel oil in a stream of compressed air. It has an upstream air compressor mechanically coupled to a downstream turbine and a combustion chamber in between.
Energy is released when compressed air is mixed with fuel and ignited in the combustor. The resulting gases are directed over the turbine's blades, spinning the turbine, and mechanically powering the compressor. Combined cycle designs pass waste heat to steam turbine systems. And combined heat and power (co-generation) uses waste heat for hot water production. Finally the exhaust gases are passed back to atmosphere.
Energy is used to power aircraft, trains, ships, electrical generators, and even tanks for heating.

## Slide 9: Gas engine
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
  Internal combustion engines operating on same principles as petrol and diesel automotive counterparts.
  Units available from 5 kWe to more than 1,000 kWe.
  Higher electrical efficiency than turbines, but thermal energy is generally at lower temperatures.
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
Most small-scale cogeneration units are internal combustion engines operating on the same familiar principles as their petrol and diesel automotive counterparts. Engines run with liquid or gaseous fuels, such as heating oil, natural gas or biogas, and are available from 5 kWe to more than 1,000 kWe. Internal combustion engines have a higher electrical efficiency than turbines, but the thermal energy they produce is generally at lower temperatures and so they are highly suited to buildings applications. The usable heat to power ratio is normally in the range 1:1 to 2:1.

## Slide 10: Gas engine - scheme
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
I
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>

## Slide 11: Heating oil engine
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
  Should only be used, if biogas or natural gas is not available!
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
Heating oil causes more green house gas, nitrogen oxide, sulphur and unburned fuel emissions than the usage of biogas and natural gas. Therefore biogas and natural gas should be preferred. Please refer to chapter 3 alternative fuels for more information.

## Slide 12: Heating oil engine - picture
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
Picture: 5 kWe heating oil engine in a Municipality house (Amel - Belgium)
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>

## Slide 13: Biogas engine
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
  If biogas is available, it is ecologically and economically reasonable to use a biogas engine!
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
Biogas is produced by fermentation under anaerobic conditions from organic substances containing water. Organic substances can be agricultural waste, maize and organic waste from industry, households and waste water. Biogas consists mainly of methane (a green house gas) and occur by fertilisation processes, waste and waste water treatment. Therefore using biogas for heat and power production is ecologically and economically reasonable. Additionally biogas causes less green house gas emissions than the usage of heating oil and natural gas. Please refer to chapter 3 alternative fuels for more information.

## Slide 14: Biogas engine – pictures
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
Picture: 102 kWe biogas engine in a small village (La Surizée - Belgium)
Picture: 1.25 MWe biogas engine in a Food Industry Lutosa (Electrabel – Belgium)
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>

## Slide 15: Steam turbine
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
  Technology has been used for large-scale cogeneration for many years.
  Range of units available: starting with ~200 kWe.
  Overall efficiency generally high, achieving up to 84%.
  Operated with: solid, liquid or gaseous fuels (also renewable).
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
Steam turbines have been used as prime movers for large-scale cogeneration systems for many years. Typically, steam turbines are associated with larger power stations but also smaller units starting with 200 kWe are frequently used. The overall efficiency generally is very high, achieving up to 84%. Steam turbines run with solid, liquid or gaseous fuels, both fossil and renewable. The typical heat to power ratio of steam turbines is around 6:1.

## Slide 16: Steam turbine - scheme
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
I
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>

## Slide 17: Stirling engine
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
  These engines are external combustion devices – different to conventional.
  Small-scale applications from 0.2 to 9 kWe available only.
  Require little maintenance, emissions of pollutants are low (depending on energy source - usually natural gas).
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
B
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
For very small-scale applications with a capacity between 0.2 kWe and 9 kWe, Stirling engines can be used. These engines are external combustion devices and therefore differ substantially from the conventional models. The Stirling engine has fewer moving parts than conventional engines, and no valves, tappets, fuel injectors or spark ignition systems. It is therefore quieter than normal engines. Stirling engines also require little maintenance and the emission of pollutants is low.

## Slide 18: Stirling engine - scheme
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Source: COGENchallenge: Pick the right cogeneration technology. 2006.
I
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>
These engines are external combustion devices and therefore differ substantially from the conventional models. The Stirling engine has fewer moving parts than conventional engines, and no valves, tappets, fuel injectors or spark ignition systems. It is therefore quieter than normal engines. Stirling engines also require little maintenance and the emission of pollutants is low.

## Slide 19: Contact
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
COGEN Europe
  Gulledelle 98, B-1200 Brussels
  Tel: +32 2 772 82 90
  Stefan Craenen
  stefan.craenen@cogen.org
Graz Energy Agency Ltd.
  National Info Point for cogeneration
  Kaiserfeldgasse 13/1, A-8010 Graz
  Tel: +43 316 811 848
  Daniel Schinnerl, Jan W. Bleyl
  schinnerl@grazer-ea.at
Notes: H2 Training Manual
30.07.26
© Graz Energy Agency - For requests: schinnerl@grazer-ea.at
Page <number>